User Manual

About this Manual

This Manual is applicable to Network Video Recorder (NVR).

The Manual includes instructions for using and managing the product. Pictures, charts, images and all other information hereinafter are for description and explanation only. The information contained in the Manual is subject to change, without notice, due to firmware updates or other reasons. Please find the latest version in the company website.

Please use this user manual under the guidance of professionals.

Legal Disclaimer

TO THE MAXIMUM EXTENT PERMITTED BY APPLICABLE LAW, THE PRODUCT DESCRIBED, WITH ITS HARDWARE, SOFTWARE AND FIRMWARE, IS PROVIDED “AS IS”, WITH ALL FAULTS AND ERRORS, AND OUR COMPANY MAKES NO WARRANTIES, EXPRESS OR IMPLIED, INCLUDING WITHOUT LIMITATION, MERCHANTABILITY, SATISFACTORY QUALITY, FITNESS FOR A PARTICULAR PURPOSE, AND NON-INFRINGEMENT OF THIRD PARTY. IN NO EVENT WILL OUR COMPANY, ITS DIRECTORS, OFFICERS, EMPLOYEES, OR AGENTS BE LIABLE TO YOU FOR ANY SPECIAL, CONSEQUENTIAL, INCIDENTAL, OR INDIRECT DAMAGES, INCLUDING, AMONG OTHERS, DAMAGES FOR LOSS OF BUSINESS PROFITS, BUSINESS INTERRUPTION, OR LOSS OF DATA OR DOCUMENTATION, IN CONNECTION WITH THE USE OF THIS PRODUCT, EVEN IF OUR COMPANY HAS BEEN ADVISED OF THE POSSIBILITY OF SUCH DAMAGES.

REGARDING TO THE PRODUCT WITH INTERNET ACCESS, THE USE OF PRODUCT SHALL BE WHOLLY AT YOUR OWN RISKS. OUR COMPANY SHALL NOT TAKE ANY RESPONSIBILITES FOR ABNORMAL OPERATION, PRIVACY LEAKAGE OR OTHER DAMAGES RESULTING FROM CYBER ATTACK, HACKER ATTACK, VIRUS INSPECTION, OR OTHER INTERNET SECURITY RISKS; HOWEVER, OUR COMPANY WILL PROVIDE TIMELY TECHNICAL SUPPORT IF REQUIRED.

SURVEILLANCE LAWS VARY BY JURISDICTION. PLEASE CHECK ALL RELEVANT LAWS IN YOUR JURISDICTION BEFORE USING THIS PRODUCT IN ORDER TO ENSURE THAT YOUR USE CONFORMS THE APPLICABLE LAW. OUR COMPANY SHALL NOT BE LIABLE IN THE EVENT THAT THIS PRODUCT IS USED WITH ILLEGITIMATE PURPOSES.

IN THE EVENT OF ANY CONFLICTS BETWEEN THIS MANUAL AND THE APPLICABLE LAW, THE LATER PREVAILS.

Regulatory Information

FCC Information

Please take attention that changes or modification not expressly approved by the party responsible for compliance could void the user’s authority to operate the equipment.

FCC compliance: This equipment has been tested and found to comply with the limits for a Class A digital device, pursuant to part 15 of the FCC Rules. These limits are designed to provide reasonable protection against harmful interference when the equipment is operated in a commercial environment. This equipment generates, uses, and can radiate radio frequency energy and, if not installed and used in accordance with the instruction manual, may cause harmful interference to radio communications. Operation of this equipment in a residential area is likely to cause harmful interference in which case the user will be required to correct the interference at his own expense.

FCC Conditions

This device complies with part 15 of the FCC Rules. Operation is subject to the following two conditions:

1. This device may not cause harmful interference.

2. This device must accept any interference received, including interference that may cause undesired operation.

EU Conformity Statement

This product and - if applicable - the supplied accessories too are marked with "CE" and comply therefore with the applicable harmonized European standards listed under the EMC Directive 2014/30/EU, the LVD Directive 2014/35/EU, the RoHS Directive 2011/65/EU.

2012/19/EU (WEEE directive): Products marked with this symbol cannot be disposed of as unsorted municipal waste in the European Union. For proper recycling, return this product to your local supplier upon the purchase of equivalent new equipment, or dispose of it at designated collection points. For more information see: www.recyclethis.info

2006/66/EC (battery directive): This product contains a battery that cannot be disposed of as unsorted municipal waste in the European Union. See the product documentation for specific battery information. The battery is marked with this symbol, which may include lettering to indicate cadmium (Cd), lead (Pb), or mercury (Hg). For proper recycling, return the battery to your supplier or to a designated collection point. For more information see: www.recyclethis.info

Industry Canada ICES-003 Compliance

This device meets the CAN ICES-3 (A)/NMB-3(A) standards requirements.

Applicable Models

This manual is applicable to the models listed in the following table.

| Series | Model |
| --- | --- |
| DS-9600NI-I8 | DS-9608NI-I8 |
|  | DS-9616NI-I8 |
|  | DS-9632NI-I8 |
|  | DS-9664NI-I8 |
| DS-9600NI-I16 | DS-9616NI-I16 |
|  | DS-9632NI-I16 |
|  | DS-9664NI-I16 |
| DS-7600NI-I2 | DS-7608NI-I2 |
|  | DS-7616NI-I2 |
|  | DS-7632NI-I2 |
| DS-7600NI-I2/P | DS-7608NI-I2/8P |
|  | DS-7616NI-I2/16P |
|  | DS-7632NI-I2/16P |
| DS-7700NI-I4 | DS-7708NI-I4 |
|  | DS-7716NI-I4 |
|  | DS-7732NI-I4 |
| DS-7700NI-I4/P | DS-7708NI-I4/8P |
|  | DS-7716NI-I4/16P |
|  | DS-7732NI-I4/16P |

Symbol Conventions

The symbols that may be found in this document are defined as follows.

| Symbol | Description |
| --- | --- |
|  | Provides additional information to emphasize or supplement important points of the main text. |
|  | Indicates a potentially hazardous situation, which if not avoided, could result in equipment damage, data loss, performance degradation, or unexpected results. |
|  | Indicates a hazard with a high level of risk, which if not avoided, will result in death or serious injury. |

Safety Instructions

Proper configuration of all passwords and other security settings is the responsibility of the installer and/or end-user.

In the use of the product, you must be in strict compliance with the electrical safety regulations of the nation and region. Please refer to technical specifications for detailed information.

Input voltage should meet both the SELV (Safety Extra Low Voltage) and the Limited Power Source with 100~240 VAC, 48 VDC or 12 VDC according to the IEC60950-1 standard. Please refer to technical specifications for detailed information.

Do not connect several devices to one power adapter as adapter overload may cause over-heating or a fire hazard.

Please make sure that the plug is firmly connected to the power socket.

If smoke, odor or noise rise from the device, turn off the power at once and unplug the power cable, and then please contact the service center.

Preventive and Cautionary Tips

Before connecting and operating your device, please be advised of the following tips:

Ensure unit is installed in a well-ventilated, dust-free environment.

Unit is designed for indoor use only.

Keep all liquids away from the device.

Ensure environmental conditions meet factory specifications.

Ensure unit is properly secured to a rack or shelf. Major shocks or jolts to the unit as a result of dropping it may cause damage to the sensitive electronics within the unit.

Use the device in conjunction with an UPS if possible.

Power down the unit before connecting and disconnecting accessories and peripherals.

A factory recommended HDD should be used for this device.

Improper use or replacement of the battery may result in hazard of explosion. Replace with the same or equivalent type only. Dispose of used batteries according to the instructions provided by the battery manufacturer.

Product Key Features

General

Connectable to network cameras, network dome and encoders

Connectable to the third-party network cameras like Acti, Arecont, Axis, Bosch, Brickcom, Canon, Panasonic, Pelco, Samsung, Sanyo. Sony, Vivotek and Zavio, and cameras that adopt ONVIF or PSIA protocol

Connectable to smart IP cameras

H.265+/H.265/ H.264+/H.264/MPEG4 video formats

PAL/NTSC adaptive video inputs

Each channel supports dual-stream

Up to 8/16/32/64 network cameras can be added according to model

Independent configuration for each channel, including resolution, frame rate, bit rate, image quality, etc.

The quality of the input and output record is configurable

Local Monitoring

HDMI/VGA1 and HDMI2/VGA2 outputs provided

HDMI video output at up to 4K resolution

Multi-screen display in live view is supported, and the display sequence of channels is adjustable

Live view screen can be switched in groups. Manual switch and auto-switch are provided and the auto-switch interval is configurable

Custom window-division live view layout configuration

3D positioning in live view

Configurable main stream and sub-stream for the live view

Quick setting menu is provided for live view

POS information overlay on live view

Motion detection, video tampering, video exception alert and video loss alert functions

Privacy mask

Multiple PTZ protocols supported; PTZ preset, patrol and pattern

Zooming in by clicking the mouse and PTZ tracing by dragging mouse

HDD Management

Up to 16 SATA hard disks and 1 eSATA disk can be connected for I16 models, and up to 8 SATA hard disks and 1 eSATA disk can be connected for I8 and K8 models

Up to 8 TB storage capacity for each disk supported

8 network disks (NAS/IP SAN disk)

S.M.A.R.T. and bad sector detection

HDD group management

Supports HDD standby function

HDD property: redundancy, read-only, read/write (R/W)

HDD quota management; different capacities can be assigned to different channels

RAID 0, RAID 1, RAID 5, RAID 6 and RAID 10 are supported

Hot-swappable RAID storage scheme can be enabled and disabled upon demand. 16 arrays can be configured

Disk clone to the eSATA disk

HDD health monitoring

Recording, Capture and Playback

Holiday recording schedule configuration

Continuous and event video recording parameters

Multiple recording types: manual, continuous, alarm, motion, motion | alarm, motion & alarm VCA, and POS

Eight recording time periods with separated recording types

POS information overlay on image

Pre-record and post-record for alarm, motion detection for recording, and pre-record time for schedule and manual recording

Searching record files and captured pictures by events (alarm input/motion detection)

Tag adding for record files, searching and playing back by tags

Locking and unlocking record files

Local redundant recording and capture

Normal/Smart/custom video playback mode

Playback by video synopsis

Searching and playing back record files by channel number, recording type, start time, end time, etc.

Supports playback by main stream or sub stream

Smart search for the selected area in the video

Zooming in when playback

Reverse playback of multi-channel

Supports pause, play reverse, speed up, speed down, skip forward, and skip backward when playback, and locating by dragging the mouse

Supports thumbnails view and fast view during playback

Up to 16-ch synchronous playback at 1080p real time

Supports playback by transcoded stream

Manual capture, continuous capture of video images and playback of captured pictures

Supports enabling H.264+ to ensure high video quality with lowered bitrate

Files Management

Search and export vehicle detection files and human appearance files

Export video data by USB, SATA or eSATA device

Export video clips when playback

Either Normal or Hot Spare working mode is configurable to constitute an N+1 hot spare system

Alarm and Exception

Configurable arming time of alarm input/output

Alarm for video loss, motion detection, tampering, abnormal signal, video input/output standard mismatch, illegal login, network disconnected, IP confliction, abnormal record/capture, HDD error, and HDD full, etc.

POS triggered alarm

VCA detection alarm is supported

Smart analysis for people counting and heat map

Connectable to the thermal network camera

Alarm triggers full screen monitoring, audio alarm, notifying surveillance center, sending e-mail and alarm output

Automatic restore when system is abnormal

Other Local Functions

Operable by front panel, mouse, remote control, or control keyboard

Three-level user management; admin user is allowed to create many operating accounts and define their operating permission, which includes the limit to access any channel

Admin password resetting by exporting/importing a GUID file

Operation, alarm, exceptions, and log recording and searching

Manually triggering and clearing alarms

Import and export device configuration information

Network Function

Two self-adaptive 10M/100M/1000 Mbps network interfaces

IPv6 is supported

TCP/IP protocol, DHCP, DNS, DDNS, NTP, SADP, SMTP, NFS, and iSCSI are supported

TCP, UDP and RTP for unicast

Auto/Manual port mapping by UPnPTM

Support access by Guarding Vision

Remote Web browser access by HTTPS ensures high security

ANR (Automatic Network Replenishment) function is supported, which enables the IP camera to save the recording files in the local storage when the network is disconnected, and synchronizes the files to the device when the network is resumed

Remote reverse playback via RTSP

Supports accessing the platform via ONVIF

Remote search, playback, download, locking and unlocking of the record files, and supports downloading files upon broken transfer resume

Remote parameters setup; remote import/export of device parameters

Remote viewing of the device status, system logs and alarm status

Remote keyboard operation

Remote HDD formatting and program upgrading

Remote system restart and shutdown

RS-232, RS-485 transparent channel transmission

Alarm and exception information can be sent to the remote host

Remotely start/stop recording

Remotely start/stop alarm output

Remote PTZ control

Remote JPEG capture

Virtual host function to access and manage the IP camera directly

Two-way audio and voice broadcasting

Embedded Web server

Development Scalability

SDK for Windows system

Source code of application software for demo

Development support and training for application system

TABLE OF CONTENTS

Chapter 1 Introduction	17

1.1 Front Panel	17

1.1.1 DS-9600NI Series	17

1.1.2 DS-7700NI Series	21

1.1.3 DS-7600NI Series	23

1.2 IR Remote Control Operations	23

1.3 USB Mouse Operation	29

1.4 Rear Panel	30

1.4.1 DS-9600NI Series	30

1.4.2 DS-7600NI Series	31

1.4.3 DS-7700NI Series	33

Chapter 2 Getting Started	35

2.1 Start up the Device	35

2.2 Activate the Device	35

2.3 Configure Login Unlock Pattern	37

2.4 Login to the Device	38

2.4.1 Log in via Unlock Pattern	38

2.4.2 Log in via a Password	38

2.5 Start Setup Wizard	39

2.6 Enter Main Menu	43

2.7 System Operation	44

2.7.1 Log out	44

2.7.2 Shut Down the Device	44

2.7.3 Reboot the Device	44

Chapter 3 Camera Management	45

3.1 Add IP Cameras	45

3.1.1 Add IP Cameras Manually	45

3.1.2 Add the Automatically Searched Online IP Cameras	46

3.2 Manage Cameras for PoE Device	46

3.2.1 Add PoE Cameras	47

3.2.2 Add Non-PoE IP Cameras	47

3.2.3 Configure PoE Interface	47

3.3 Enable the H.265 Stream Access	49

3.4 Upgrade the IP Camera	49

3.5 Configure the Customized Protocols	49

Chapter 4 Camera Settings	51

4.1 Configure OSD Settings	51

4.2 Configure Privacy Mask	52

4.3 Configure the Image Parameters	53

4.4 Configure the Day/Night Switch	53

4.5 Configure Other Camera Parameters	53

Chapter 5 Live View	55

5.1 Start Live View	55

5.1.1 Digital Zoom	55

5.1.2 Fisheye View	55

5.1.3 3D Positioning	56

5.1.4 Live View Strategy	56

5.2 Target Detection	57

5.3 Configure Live View Settings	57

5.4 Configure Live View Layout	58

5.4.1 Configure Custom Live View Layout	58

5.4.2 Configure Live View Mode	59

5.5 Configure Camera Auto-Switch	60

5.6 Configure Channel-Zero Encoding	60

Chapter 6 PTZ Control	62

6.1 PTZ Control Wizard	62

6.2 ConfigurePTZ Parameters	62

6.3 Set PTZ Presets, Patrols, and Patterns	63

6.3.1 Set Presets	63

6.3.2 Call Presets	64

6.3.3 Set Patrols	65

6.3.4 Call a Patrol	66

6.3.5 Set a Pattern	67

6.3.6 Call a Pattern	67

6.3.7 Set Linear Scan Limits	68

6.3.8 Call Linear Scan	69

6.3.9 One-Touch Park	69

6.4 Auxiliary Functions	70

Chapter 7 Storage	71

7.1 Storage Device Management	71

7.1.1 Install the HDD	71

7.1.2 Add the Network Disks	71

7.1.3 Configure eSATA for Data Storage	73

7.2 Storage Mode	74

7.2.1 Configure HDD Groups	74

7.2.2 Configure HDD Quota	76

7.3 Recording Parameters	77

7.3.1 Main Stream	77

7.3.2 Sub-Stream	77

7.3.3 Picture	78

7.3.4 ANR	78

7.3.5 Configure Advanced Recording Settings	78

7.4 Configure Recording Schedule	79

7.5 Configure Continuous Recording	81

7.6 Configure Motion Detection Triggered Recording	81

7.7 Configure Event Triggered Recording	82

7.8 Configure Alarm Triggered Recording	82

7.9 Configure POS Event Triggered Recording	83

7.10 Configure Picture Capture	83

7.11 Configure Holiday Recording and Capture	83

7.12 Configure Redundant Recording and Capture	85

Chapter 8 Disk Array (RAID)	87

8.1 Create a Disk Array	87

8.1.1 Enable a RAID	87

8.1.2 One-Touch Creation	88

8.1.3 Manual Creation	88

8.2 Rebuild an Array	90

8.2.1 Configure a Hot Spare Disk	90

8.2.2 Automatically Rebuild an Array	90

8.2.3 Manually Rebuild an Array	91

8.3 Delete an Array	92

8.4 Check and Edit Firmware	93

Chapter 9 File Management	94

9.1 Search and Export All Files	94

9.1.1 Search Files	94

9.1.2 Export Files	94

9.2 Search and Export Human Files	95

9.2.1 Search Human Files	95

9.2.2 Export Human Files	95

9.3 Search and Export Vehicle Files	96

9.3.1 Search Vehicle Files	96

9.3.2 Export Vehicle Files	96

9.4 Search History Operation	97

9.4.1 Save Search Conditions	97

9.4.2 Call Search History	97

Chapter 10 Playback	98

10.1 Play Video Files	98

10.1.1 Instant Playback	98

10.1.2 Play Normal Video	98

10.1.3 Play Smart Searched Video	99

10.1.4 Play Custom Searched Files	100

10.1.5 Play Tag Files	101

10.1.6 Play Event Files	103

10.1.7 Play Video Synopsis	105

10.1.8 Play by Sub-periods	105

10.1.9 Play Log Files	106

10.1.10 Play External Files	107

10.2 Playback Operations	107

10.2.1 Set Play Strategy in Smart/Custom Mode	107

10.2.2 Edit Video Clips	108

10.2.3 Switch between Main Stream and Sub-Stream	108

10.2.4 Thumbnails View	109

10.2.5 Fisheye View	109

10.2.6 Fast View	110

10.2.7 Digital Zoom	110

10.2.8 POS Information Overlay	110

Chapter 11 Event and Alarm Settings	111

11.1 Configure Arming Schedule	111

11.2 Configure Alarm Linkage Actions	111

11.3 Configure Motion Detection Alarms	113

11.4 Configure Video Loss Alarms	115

11.5 Configure Video Tampering Alarms	116

11.6 Configure Sensor Alarms	117

11.6.1 Configure Alarm Inputs	117

11.6.2 Configure One-Key Disarming	117

11.6.3 Configure Alarm Outputs	118

11.7 Configure Exceptions Alarms	120

11.8 Setting Alarm Linkage Actions	122

11.8.1 Configure Auto-Switch Full Screen Monitoring	122

11.8.2 Configure Audio Warning	122

11.8.3 Notify Surveillance Center	123

11.8.4 Configure E-mail Linkage	123

11.8.5 Trigger Alarm Outputs	123

11.8.6 Configure PTZ Linkage	123

11.9 Trigger or Clear Alarm Output Manually	124

Chapter 12 VCA Event Alarm	126

12.1 Face Detection	126

12.2 Vehicle Detection	127

12.3 Line Crossing Detection	128

12.4 Intrusion Detection	129

12.5 Region Entrance Detection	131

12.6 Region Exiting Detection	132

12.7 Unattended Baggage Detection	133

12.8 Object Removal Detection	134

12.9 Audio Exception Detection	135

12.10 Sudden Scene Change Detection	136

12.11 Defocus Detection	137

12.12 PIR Alarm	138

12.13 Thermal Camera Detection	140

Chapter 13 Smart Analysis	141

13.1 People Counting	141

13.2 Heat Map	141

Chapter 14 POS Configuration	143

14.1 Configure POS Settings	143

14.1.1 Configure POS Connection	143

14.1.2 Configure POS Text Overlay	147

14.2 Configure POS Alarm	148

Chapter 15 Network Settings	149

15.1 Configure TCP/IP Settings	149

15.1.1 Device with Dual Network Interface	149

15.1.2 Device with a Single Network Interface	150

15.2 Configure Guarding Vision	151

15.3 Configure DDNS	153

15.4 Configure PPPoE	154

15.5 Configure NTP	154

15.6 Configure SNMP	155

15.7 Configure Email	156

15.8 Configure Ports	157

Chapter 16 Hot Spare Device Backup	159

16.2 Set Hot Spare Device	159

16.3 Set Working Device	160

16.4 Manage Hot Spare System	160

Chapter 17 User Management and Security	162

17.1 Manage User Accounts	162

17.1.1 Add a User	162

17.1.2 Edit the Admin User	164

17.1.3 Edit an Operator/Guest User	165

17.1.4 Delete a User	166

17.2 Manage User Permissions	166

17.2.1 Set User Permissions	166

17.2.2 Set Local Live View Permission for Non-Admin Users	168

17.2.3 Set Live View Permission on Lock Screen	169

17.3 Configure Password Security	170

17.3.1 Export GUID File	170

17.3.2 Configure Security Questions	171

17.4 Reset Password	172

17.4.1 Reset Password by GUID	172

17.4.2 Reset Password by Security Questions	173

Chapter 18 System Service Maintenance	174

18.1 Storage Device Maintenance	174

18.1.1 Configure Disk Clone	174

18.1.2 S.M.A.R.T. Detection	175

18.1.3 Bad Sector Detection	176

18.1.4 HDD Health Detection	177

18.2 Search and Export Log Files	178

18.2.1 Search the Log Files	178

18.2.2 Export the Log Files	179

18.3 Import/Export IP Camera Configuration Files	180

18.4 Import/Export Device Configuration Files	182

18.5 Configure System Services	182

18.5.1 Control4 Protocol	182

18.5.2 I-VIEW-NOW UPNP Reporting	183

18.6 Configure Stream Encryption	183

18.7 Upgrade the System	184

18.7.1 Upgrade with a Local Backup Device	184

18.7.2 Upgrade by FTP	184

18.8 Restore Default Settings	186

Chapter 19 General System Settings	187

19.1 Configure General Settings	187

19.2 Configure Date & Time	188

19.3 Configure DST Settings	189

Chapter 20 Appendix	190

20.1 Glossary	190

20.2 Troubleshooting	192

20.3 Summary of Changes	200

Version 4.1.50	200

Version 4.1.10	200

Version 4.1.0	200

Version 3.4.92	200

Version 3.4.91	200

Version 3.4.90	200

Version 3.4.80	201

Version 3.4.70	201

Version 3.4.6	201

Version 3.4.2	201

Version 3.3.9	202

Version 3.3.7	202

Version 3.3.6	202

Version 3.3.4	202

20.4 List of IP Cameras Connected to PoE by Long Network Cable (100 - 300 m)	203

# Introduction

## Front Panel

### DS-9600NI Series

DS-9600NI-I8 Series

DS-9600NI-I16 Series

Panel Description

| No. | Name | Function Description |
| --- | --- | --- |
| 1 | Status Indicators | ALARM | Turns red when a sensor alarm is detected. |
|  |  | READY | Turns blue when the device is functioning properly. |
|  |  | STATUS | Turns blue when device is controlled by an IR remote. |
|  |  |  | Turns red when controlled by a keyboard and purple when IR remote and keyboard is used at the same time. |
|  |  | HDD | Flickers red when data is being read from or written to HDD. |
|  |  | MODEM | Reserved for future usage. |
|  |  | Tx/Rx | Flickers blue when network connection is functioning properly. |
|  |  | GUARD | Turns blue when the device is in armed status; at this time, an alarm is enabled when an event is detected. |
|  |  |  | Turns off when the device is unarmed. The arm/disarm status can be changed by pressing and holding on the ESC button for more than 3 seconds in live view mode. |
| 2 | IR Receiver | Receiver for IR remote control. |
| 3 | Front Panel Lock | Locks or unlocks the panel by the key. |
| 4 | DVD-R/W | Slot for DVD-R/W disk. |
| 5 | Alphanumeric Buttons | Switches to the corresponding channel in live view or PTZ control mode. |
|  |  | Inputs numbers and characters in edit mode. |
|  |  | Switches between different channels in playback mode. |
|  |  | Turns blue when the corresponding channel is recording; turns red when the channel is in network transmission status; turns pink when the channel is recording and transmitting. |
| 6 | USB Interfaces | Universal Serial Bus (USB) ports for additional devices such as USB mouse and USB Hard Disk Drive (HDD). |
| 7 | Composite Keys | ESC | Returns to the previous menu. |
|  |  |  | Presses for arming/disarming the device in live view mode. |
|  |  | REC/SHOT | Enters the Manual Record settings menu. |
|  |  |  | Presses this button followed by a numeric button to call a PTZ preset in PTZ control settings. |
|  |  |  | Turns audio on/off in the playback mode. |
|  |  | PLAY/AUTO | Enters the playback mode. |
|  |  |  | Automatically scans in the PTZ control menu. |
|  |  | ZOOM+ | Zooms in the PTZ camera in the PTZ control setting. |
|  |  | A/FOCUS+ | Adjusts focus in the PTZ Control menu. |
|  |  |  | Switches between input methods (upper and lower case alphabet, symbols and numeric input). |
|  |  | EDIT/IRIS+ | Edits text fields. When editing text fields, it also deletes the character in front of the cursor. |
|  |  |  | Checks the checkbox in the checkbox fields. |
|  |  |  | Adjusts the iris of the camera in PTZ control mode. |
|  |  |  | Generates video clips for backup in playback mode. |
|  |  |  | Enters/exits the folder of USB device and eSATA HDD. |
|  |  | MAIN/SPOT/ZOOM- | Switches between main and spot output. |
|  |  |  | Zooms out the image in PTZ control mode. |
|  |  | F1/ LIGHT | Selects all items on the list when used in a list field. |
|  |  |  | Turns on/off PTZ light (if applicable) in PTZ control mode. |
|  |  |  | Switches between play and reverse play in playback mode. |
|  |  | F2/ AUX | Cycles through tab pages. |
|  |  |  | Switches between channels in synchronous playback mode. |
|  |  | MENU/WIPER | Returns to the Main menu (after successful login). |
|  |  |  | Presses and holds the button for five seconds to turn off audible key beep. |
|  |  |  | Starts wiper (if applicable) in PTZ control mode. |
|  |  |  | Shows/hides the control interface in playback mode. |
|  |  | PREV/FOCUS- | Switches between single screen and multi-screen mode. |
|  |  |  | Adjusts the focus in conjunction with the A/FOCUS+ button in PTZ control mode. |
|  |  | PTZ/IRIS- | Enters the PTZ Control mode. |
|  |  |  | Adjusts the iris of the PTZ camera in PTZ control mode. |
| 8 | Control Buttons | DIRECTION | Navigates between different fields and items in menus. |
|  |  |  | In the playback mode, use the Up and Down buttons to speed up and slow down recorded video. Use the Left and Right buttons to select the next and previous video files. |
|  |  |  | Cycles through channels in live view mode. |
|  |  |  | Controls the movement of the PTZ camera in PTZ control mode. |
|  |  | ENTER | Confirms selection in any of the menu modes. |
|  |  |  | Checks the checkbox fields. |
|  |  |  | Plays or pauses the video playing in playback mode. |
|  |  |  | Advances the video by a single frame in single-frame playback mode. |
|  |  |  | Stops/starts auto switch in auto-switch mode. |
| 9 | JOG SHUTTLE Control | Moves the active selection up and down in a menu. |
|  |  | Cycles through different channels in live view mode. |
|  |  | Jumps 30s forward/backward in video files in the playback mode. |
|  |  | Controls the movement of the PTZ camera in PTZ control mode. |
| 10 | POWER ON/OFF | Long press the button for more than 3 seconds to turn on/off the device. |

### DS-7700NI Series

DS-7700NI Series

Panel Description

| No. | Name | Function Description |
| --- | --- | --- |
| 1 | Status Indicators | POWER | Turns green when device is powered up. |
|  |  | HDD | Blinks red when HDD is reading/writing. |
|  |  | Tx/Rx | Blinks green when network connection is functioning normally. |
| 2 | ENTER | The Enter button is used to confirm selection in menu mode; or used to check checkbox fields and ON/OFF switch. |
|  |  | In playback mode, it can be used to play or pause the video. |
|  |  | In single-frame play mode, pressing the Enter button will play the video by a single frame. |
|  |  | In auto sequence view mode, the buttons can be used to pause or resume auto sequence. |
|  |  | The Enter button is used to confirm selection in menu mode; or used to check checkbox fields and ON/OFF switch. |
| 3 | DIRECTION | In menu mode, the direction buttons are used to navigate between different fields and items and select setting parameters. |
|  |  | In playback mode, the Up and Down buttons are used to speed up and slow down record playing, and the Left and Right buttons are used to move the recording 30s forwards or backwards. |
|  |  | In the image setting interface, the up and down button can adjust the level bar of the image parameters. In live view mode, these buttons can be used to switch channels. |
| 4 | Back | Back to the previous menu. |
| 5 | POWER ON/OFF | Power on/off switch. |
| 6 | MENU | Access the main menu interface. |
| 7 | USB Interface | Universal Serial Bus (USB) ports for additional devices such as USB mouse and USB Hard Disk Drive (HDD). |

### DS-7600NI Series

DS-7600NI Series

Panel Description

| No. | Name | Connections |
| --- | --- | --- |
| 1 | POWER | Turns green when device is powered up. |
| 2 | HDD | Flickers red when data is being read from or written to HDD. |
| 3 | Tx/Rx | Flickers blue when network connection is functioning properly. |
| 4 | USB Interface | Universal Serial Bus (USB) port for additional devices such as USB mouse and USB Hard Disk Drive (HDD). |

## IR Remote Control Operations

The device may also be controlled with the included IR remote control, shown in Figure 1-5.

Batteries (2×AAA) must be installed before operation.

The IR remote is set at the factory to control the device (using default Device ID# 255) without any additional steps. Device ID# 255 is the default universal device identification number shared by the devices. You may also pair an IR Remote to a specific device by changing the Device ID#, as follows:

Pairing (Enabling) the IR Remote to a Specific Device (optional)

You can pair an IR Remote to a specific device by creating a user-defined Device ID#. This feature is useful when using multiple IR Remotes and devices.

On the device:

Go to System > General.

Type a number (255 digits maximum) into the Device No. field.

On the IR Remote:

Press the DEV button.

Use the Number buttons to enter the Device ID# that was entered into the device.

Press Enter button to accept the new Device ID#.

Remote Control

Unpairing (Disabling) an IR Remote from a Device

To unpair an IR Remote from a device so that the unit cannot control any device functions, proceed as follows:

Press the DEV key on the IR Remote. Any existing Device ID# will be erased from the unit’s memory and it will no longer function with the device.

(Re)-enabling the IR Remote requires pairing to a device. See “Pairing the IR Remote to a Specific device (optional),” above.

The keys on the remote control closely resemble the ones on the front panel. See the table 1.4.

IR Remote Functions

| No. | Name | Function Description |
| --- | --- | --- |
| 1 | POWER ON/OFF | •To Turn Power On: -If User Has Not Changed the Default device Device ID# (255): 1.Press Power On/Off button (1). -If User Has Changed the device Device ID#: 1.Press DEV button. 2.Press Number buttons to enter user-defined Device ID#. 3.Press Enter button. 4.Press Power button to start device. •To Turn device Off: -If User Is Logged On: 1.Hold Power On/Off button (1) down for five seconds to display the “Yes/No” verification prompt. 2.Use Up/Down Arrow buttons (12) to highlight desired selection. 3.Press Enter button (12) to accept selection. -If User Is Not Logged On: 1.Hold Power On/Off button (1) down for five seconds to display the user name/password prompt. 2.Press the Enter button (12) to display the on-screen keyboard. 3.Input the user name. 4.Press the Enter button (12) to accept input and dismiss the on-screen keyboard. 5.Use the Down Arrow button (12) to move to the “Password” field. 6.Input password (use on-screen keyboard or numeric buttons (3) for numbers). 7.Press the Enter button (12) to accept input and dismiss the on-screen keyboard. 8.Press the OK button on the screen to accept input and display the Yes/No” verification prompt (use Up/Down Arrow buttons (12) to move between fields) 9.Press Enter button (12) to accept selection. User name/password prompt depends on device is configuration. See “System Configuration” section. |
| 2 | DEV | Enable IR Remote: Press DEV button, enter device Device ID# with number keys, press Enter to pair unit with the device |
|  |  | Disable IR Remote: Press DEV button to clear Device ID#; unit will no longer be paired with the device |
| 3 | Numerals | Switch to the corresponding channel in Live View or PTZ Control mode |
|  |  | Input numbers in Edit mode |
| 4 | EDIT | Delete characters before cursor |
|  |  | Check the checkbox and select the ON/OFF switch |
| 5 | A | Adjust focus in the PTZ Control menu |
|  |  | Switch on-screen keyboards (upper and lower case alphabet, symbols, and numerals) |
| 6 | REC | Enter Manual Record setting menu |
|  |  | Call a PTZ preset by using the numeric buttons in PTZ control settings |
|  |  | Turn audio on/off in Playback mode |
| 7 | PLAY | Go to Playback mode |
|  |  | Auto scan in the PTZ Control menu |
| 8 | INFO | Reserved |
| 9 | VOIP | Switches between main and spot output Zooms out the image in PTZ control mode |
| 10 | MENU | Return to Main menu (after successful login) |
|  |  | N/A |
|  |  | Show/hide full screen in Playback mode |
| 12 | DIRECTION | Navigate between fields and menu items |
|  |  | Use Up/Down buttons to speed up/slow down recorded video, and Left/Right buttons to advance/rewind 30 secs in Playback mode |
|  |  | Cycle through channels in Live View mode |
|  |  | Control PTZ camera movement in PTZ control mode |
|  | ENTER | Confirm selection in any menu mode |
|  |  | Checks checkbox |
|  |  | Play or pause video in Playback mode |
|  |  | Advance video a single frame in single-frame Playback mode |
|  |  | Stop/start auto switch in auto-switch mode |
| 13 | PTZ | Enter PTZ Control mode |
| 14 | ESC | Go back to previous screen |
|  |  | N/A |
| 15 | RESERVED | Reserved |
| 16 | F1 | Select all items on a list |
|  |  | N/A |
|  |  | Switch between play and reverse play in Playback mode |
| 17 | PTZ Control | Adjust PTZ camera iris, focus, and zoom |
| 18 | F2 | Cycle through tab pages |
|  |  | Switch between channels in Synchronous Playback mode |

Troubleshooting Remote Control:

Make sure you have installed batteries properly in the remote control. And you have to aim the remote control at the IR receiver in the front panel.

If there is no response after you press any button on the remote, follow the procedure below to troubleshoot.

          - Go to System > General by operating the front control panel or the mouse.

Check and remember device ID#. The default ID# is 255. This ID# is valid for all the IR remote controls.

Press the DEV button on the remote control.

Enter the device ID# you set in step 2.

Press the ENTER button on the remote.

If the Status indicator on the front panel turns blue, the remote control is operating properly. If the Status indicator does not turn blue and there is still no response from the remote, please check the following:

Batteries are installed correctly and the polarities of the batteries are not reversed.

Batteries are fresh and not out of charge.

IR receiver is not obstructed.

No fluorescent lamp is used nearby

If the remote still can’t function properly, please change a remote and try again, or contact the device provider.

## USB Mouse Operation

A regular 3-button (Left/Right/Scroll-wheel) USB mouse can also be used with this device. To use a USB mouse:

Plug USB mouse into one of the USB interfaces on the front panel of the device.

The mouse should automatically be detected. If in a rare case that the mouse is not detected, the possible reason may be that the two devices are not compatible, please refer to the recommended the device list from your provider.

The operation of the mouse:

Description of the Mouse Control

| Name | Action | Description |
| --- | --- | --- |
| Left-Click | Single-Click | Live view: Select channel and show the quick set menu. Menu: Select and enter. |
|  | Double-Click | Live view: Switch between single-screen and multi-screen. |
|  | Click and Drag | PTZ control: pan, tilt and zoom. Video tampering, privacy mask and motion detection: Select target area. Digital zoom-in: Drag and select target area. Live view: Drag channel/time bar. |
| Right-Click | Single-Click | Live view: Show menu. Menu: Exit current menu to upper level menu. |
| Scroll-Wheel | Scrolling up | Live view: Previous screen. Menu: Previous item. |
|  | Scrolling down | Live view: Next screen. Menu: Next item. |

## Rear Panel

### DS-9600NI Series

DS-9600NI-I8 Series

DS-9600NI-I16 Series

Panel Description

| No. | Name | Description |
| --- | --- | --- |
| 1 | LAN1/LAN2 Interface | 2 RJ-45 10/100/1000 Mbps self-adaptive Ethernet interfaces provided. |
| 2 | LINE IN | RCA connector for audio input. |
| 3 | AUDIO OUT | 2 RCA connectors for audio output. |
| 4 | HDMI1/HDMI2 | HDMI video output connector. |
| 5 | VGA1/VGA2 | DB9 connector for VGA output. Display local video output and menu. |
| 6 | USB 3.0 interface | Universal Serial Bus (USB) ports for additional devices such as USB mouse and USB Hard Disk Drive (HDD). |
| 7 | RS-232 Interface | Connector for RS-232 devices. |
| 8 | eSATA | Connects external SATA HDD, CD/DVD-RM. |
| 9 | Controller Port | D+, D- pin connects to Ta, Tb pin of controller. For cascading devices, the first device’s D+, D- pin should be connected with the D+, D- pin of the next device. |
|  | ALARM IN | Connector for alarm input. |
|  | ALARM OUT | Connector for alarm output. |
| 10 | 100 to 240 VAC | 100 to 240 VAC power supply. |
| 11 | Power Switch | Switch for turning on/off the device. |
| 12 | GROUND | Ground (needs to be connected when device starts up). |

### DS-7600NI Series

DS-7600NI-I2 Series

DS-7600NI-I2/8P Series

The DS-7616NI-I2/16P and DS-7632NI-I2/16P provide 16 network Interfaces with PoE function.

Panel Description

| No. | Name | Description |
| --- | --- | --- |
| 1 | Audio In | RCA connector for audio input. |
| 2 | Audio Out | RCA connector for audio output. |
| 3 | VGA Interface | DB9 connector for VGA output. Display local video output and menu. |
| 4 | HDMI Interface | HDMI video output connector. |
| 5 | ALARM IN | Connector for alarm input. |
|  | ALARM OUT | Connector for alarm output. |
| 6 | LAN Network Interface | 1 10/100/1000 Mbps self-adaptive Ethernet interface |
| 7 | USB Interface | Universal Serial Bus (USB 3.0) ports for additional devices such as USB mouse and USB Hard Disk Drive (HDD). |
| 8 | Ground | Ground (needs to be connected when device starts up). |
| 9 | Power Supply | 12 VDC power supply for DS-7600NI-I4, and 100 to 240 VAC for DS-7600NI-I4/P. |
| 10 | Power Switch | Switch for turning on/off the device. |
| 11 | Network Interfaces with PoE function (for DS-7600NI-I2/P) | Network interfaces for the cameras and to provide power over Ethernet. |

### DS-7700NI Series

DS-7700NI-I4 Series

DS-7700NI-I4/16P Series

The DS-7708NI-I4/8P provides 8 network Interfaces with PoE function.

Panel Description

| No. | Name | Description |
| --- | --- | --- |
| 1 | LAN Interface | 1 network interface provided for DS-7700NI-I4/P, and 2 network interfaces for DS-7700NI-I4. |
| 2 | AUDIO OUT | RCA connector for audio output. |
| 3 | LINE IN | RCA connector for audio input. |
| 4 | HDMI | HDMI video output connector. |
| 5 | USB 3.0 interface | Universal Serial Bus (USB) ports for additional devices such as USB mouse and USB Hard Disk Drive (HDD). |
| 6 | RS-232 Interface | Connector for RS-232 devices. |
| 7 | VGA | DB9 connector for VGA output. Display local video output and menu. |
| 8 | RS-485 Interface | Half-duplex connector for RS-485 devices. |
| 9 | ALARM IN | Connector for alarm input. |
|  | ALARM OUT | Connector for alarm output. |
| 10 | GROUND | Ground (needs to be connected when device starts up). |
| 11 | AC 100V ~ 240V | 100V to 240VAC power supply. |
| 12 | Power Switch | Switch for turning on/off the device. |
| 13 | Network Interfaces with PoE function (for DS-7700NI-I4/P) | Network interfaces for the cameras and to provide power over Ethernet. |

# Getting Started

## Start up the Device

Purpose:

Proper startup and shutdown procedures are crucial to expanding the life of the device.

Before you start:

Check that the voltage of the extra power supply is the same with the device’s requirement, and the ground connection is working properly.

Start up the device:

Check the power supply is plugged into an electrical outlet. It is HIGHLY recommended that an Uninterruptible Power Supply (UPS) be used in conjunction with the device. The Power indicator LED on the front panel should be red, indicating the device gets the power supply.

Press the POWER button on the front panel. The Power indicator LED should turn blue indicating that the unit begins to start up.

After startup, the Power indicator LED remains blue. A splash screen with the status of the HDD appears on the monitor. The row of icons at the bottom of the screen shows the HDD status. ‘X’ means that the HDD is not installed or cannot be detected.

## Activate the Device

Purpose:

For the first-time access, you need to activate the device by setting an admin password. No operation is allowed before activation. You can also activate the device via Web Browser, SADP or Client Software.

Input the same password in the text field of Create New Password and Confirm New Password.

You can click  to show the characters input.

Activating the Device

We highly recommend you create a strong password of your own choosing (Using a minimum of 8 characters, including at least three of the following categories: upper case letters, lower case letters, numbers, and special characters.) in order to increase the security of your product. And we recommend you reset your password regularly, especially in the high security system, resetting the password monthly or weekly can better protect your product.

In the Create Channel Default Password text field, create a default password of IP camera (s) connected to the device.

(Optional) Check Export GUID and Security Question Configuration.

Export GUID: export the GUID for future password resetting.

Security Question Configuration: configure the security questions which can be used for resetting the password.

Click OK.

What to do next:

- When you have enabled the Export GUID, continue to export the GUID file to the USB flash driver for the future password resetting.

- When you have enabled the Security Question Configuration, continue to set the security questions for the future password resetting.

After the device is activated, you should properly keep the password.

You can duplicate the password to the IP cameras that are connected with default protocol.

## Configure Login Unlock Pattern

You can configure a device login unlock pattern for the admin user.

          - After the device is activated, enter the following interface to configure the device unlock pattern.

          - Use the mouse to draw a pattern among the 9 dots on the screen. Release the mouse when the pattern is done.

Draw the Pattern

Connect at least 4 dots to draw the pattern.

Each dot can be connected for once only.

          - Draw the same pattern again to confirm it. When the two patterns match, the pattern is configured successfully.

If the two patterns are different, you must set the pattern again.

## Login to the Device

### Log in via Unlock Pattern

Only the admin user has permission to unlock the device.

Before you Start

Configure the unlock pattern before unlocking. Refer to Chapter 2.3 Configure Login Unlock Pattern.

Right click the mouse and select the menu to enter the interface.

Draw the Unlock Pattern

Draw the pre-defined pattern to unlock and enter the menu operation.

If you have forgotten your pattern, select Forgot My Pattern or Switch User to enter the normal login dialog box.

If the pattern you draw is different from the pattern you configured, try again.

If you draw the wrong pattern more than five times, the system will switch to the normal login mode automatically.

### Log in via a Password

Purpose:

If the device has logged out, you must log in to the device before operating the menu and other functions.

Select your User Name in the drop-down list.

Login Interface

Input password.

Click Login to log in.

If you forget the admin password, click Forgot Password to reset the password.

In the Login dialog box, if you enter the wrong password 7 times, the current user account will be locked for 60 seconds.

## Start Setup Wizard

The Setup Wizard walks you through some important basic device settings.

By default, the Setup Wizard starts once the device has loaded. If you don’t want to use the Setup Wizard at that moment, click Exit.

          - Set the date and time on the Date and Time Setup interface.

Date and Time Settings

Set the basic network parameters on the Network Setup interface.

Network Settings

Select a HDD and click Init to initialize it as demand on the Hard Disk interface.

HDD Management

Add IP cameras on the Camera Setup interface.

Click Search to search online IP camera. Before adding a camera, make sure the IP camera to be added is in active status.

Click Add to add the camera.

If the camera is in inactive status, select the camera from the list and click Activate.

Search for IP Cameras

Enter Platform Access interface and configure the Guarding Vision settings.

Guarding Vision Access

Enter the Change Password interface to create a new admin password if required.

Change Password

You can enter click the  to show the characters input.

- Check the New Admin Password checkbox.

- Enter the original password in the Admin Password text field.

- Input the same password in the New Password and Confirm text fields.

- Check the Unlock Pattern checkbox to enable the login via unlock pattern.

We highly recommend you create a strong password of your own choosing (Using a minimum of 8 characters, including at least three of the following categories: upper case letters, lower case letters, numbers, and special characters.) in order to increase the security of your product. And we recommend you reset your password regularly, especially in the high security system, resetting the password monthly or weekly can better protect your product.

Click OK to complete the startup Setup Wizard.

## Enter Main Menu

After you have completed the wizard, you can right click on the screen to enter the main menu bar. Refer to the following figure and table for the description of main menu and sub-menus.

Main Menu Bar

Description of Icons

| Icon | Description |
| --- | --- |
|  | Live View |
|  | Playback |
|  | File Management |
|  | Smart Analysis |
|  | Camera Management |
|  | Storage Management |
|  | System Management |
|  | System Maintenance: |

## System Operation

### Log out

Purpose:

After logging out, the monitor turns to live view mode. To perform any operations, you need to log in again.

Click on the menu bar.

Click Logout.

After you log out of the system, menu operations on the screen are invalid. You must input a user name and password to unlock the system.

### Shut Down the Device

          - Click on the menu bar.

Click Shutdown.

Click Yes.

Do not press POWER again when the system is shutting down.

### Reboot the Device

From the Shutdown menu, you can also reboot the device.

          - Click on the menu bar.

Click Reboot to reboot the device.

# Camera Management

## Add IP Cameras

### Add IP Cameras Manually

Purpose:

Before you can view live video or record video files, you must add the network cameras to the connection list of the device.

Before You Start:

Ensure the network connection is valid and the IP camera has been activated.

          - Click  on the main menu bar to enter the Camera Management interface.

          - Click the Custom Add tab on the title bar or click  in the idle channel window to enter the Add IP Camera interface.

          - Enter IP address, protocol, management port, and other information.

          - Enter the login user name and password of the IP camera.

Add IP Camera

          - Click Add to finish adding the IP camera.

          - (Optional) Click Continue to Add to continue to add other IP cameras.

### Add the Automatically Searched Online IP Cameras

          - On the Camera Management interface, click the Online Device panel to expand the Online Device interface.

          - Select the automatically searched online device.

          - Click Add to add the camera which has the same login password with the device.

Add IP Camera

If the IP camera to add has not been actiavated, you can activate it from the IP camera list on the camera management interface.

## Manage Cameras for PoE Device

This chapter is only applicable for the following models: DS-7600NI-I2/P and DS-7700NI-I4/P series device.

Purpose:

The PoE interfaces enables the device system to pass electrical power safely, along with data, on Ethernet cabling to the connected PoE cameras. Supported PoE camera number varies with device model

If you disable the PoE interface, you can also connect to the online network cameras. And the PoE interface supports the Plug-and-Play function.

For example, for DS-7608NI-I2/8P, if you want to connect 6 network cameras via PoE interfaces and 2 online cameras, you must disable 2 PoE interfaces in the Edit IP Camera menu.

Follow the steps to add network cameras for device supporting PoE function.

### Add PoE Cameras

Connect PoE cameras to device PoE ports with network cables.

Go to Camera > Camera > IP Camera to view camera image and information.

### Add Non-PoE IP Cameras

You can disable the PoE interface by selecting the manual while the current channel can be used as a normal channel and the parameters can also be edited.

Go to Camera > Camera > IP Camera.

Position the cursor on a window with no linked IP camera and click the  button.

Edit IP Camera

Select Adding Method as Manual.

- Plug-and-Play: The camera is physically connected to the PoE interface. Its parameters cannot be edited. You can go to System > Network > TCP/IP to change IP address of PoE port.  .

- Manual: Add IP camera without physical connection via network.

Enter the IP address, the user name and password of administrator manually.

Click OK.

### Configure PoE Interface

Purpose:

When it requires long-distance PoE transmission (100 to 300 m), you can enable long distance mode for the PoE channel.

Go to Camera > Camera >PoE Settings.

Enable or disable long network cable mode by selecting Long Distance or Short Distance radio.

Long Distance: Long-distance (100 to 300 meters) network transmissions via POE interface.

Short Distance: Short-distance (< 100 meters) network transmission via POE interface.

PoE Settings

The PoE ports are enabled with the short distance mode by default.

The bandwidth of IP camera connected to the PoE via long network cable (100 to 300 meters) cannot exceed 6 MP.

The allowed max. long network cable may be less than 300 meters depending on different IP camera models and cable materials.

When the transmission distance reaches 100 to 250 meters, you must use the CAT5E or CAT6 network cable to connect with the PoE interface.

When the transmission distance reaches 250 to 300 meters, you must use the CAT6 network cable to connect with the PoE interface.

Refer to the Appendix 20.4 List of IP Cameras Connected to PoE by Long Network Cable (100 - 300 m) for the list of IP cameras.

Click Apply.

## Enable the H.265 Stream Access

The device can automatically switch to the H.265 stream of IP camera (which supports H.265 video format) for the initial access.

Go to More Settings > H.265 Auto Switch Configuration at the top taskbar.

Check the checkbox of Enable H.265 (For Initial Access).

Click OK.

## Upgrade the IP Camera

The IP camera can be remotely upgraded through the device.

Plug the U-flash drive with the IP camera’s firmware upgrade file to the device.

On the camera management interface, select a camera.

Go to More Settings > Upgrade at the top taskbar.

Select the firmware upgrade file from the U-flash drive.

Click Upgrade.

Result:

The IP camera will reboot automatically after the upgrading completes.

## Configure the Customized Protocols

Purpose

To connect the network cameras which are not configured with the standard protocols, you can configure the customized protocols for them. The system provides 16 customized protocols.

          - Go to More Settings > Protocol at the top taskbar to enter the protocol management interface.

Protocol Management

Select the protocol type of transmission and choose the transfer protocols.

Type: The network camera adopting custom protocol must support getting stream through standard RTSP.

Path: you have to contact the manufacturer of the network camera to consult the URL (uniform resource locator) for getting main stream and sub-stream.

The format of the URL is: [Type]://[IP Address of the network camera]:[Port]/[Path].

Example: rtsp://192.168.1.55:554/ch1/main/av_stream.

The protocol type and the transfer protocols must be supported by the connected IP camera.

Click OK to save the settings.

Result:

After adding the customized protocols, you can see the protocol name is listed in the drop-down list.

# Camera Settings

## Configure OSD Settings

Purpose

You can configure the OSD (On-screen Display) settings for the camera, including date/time, camera name, etc.

Go to Camera >Display.

Select the camera from the drop-down list.

Edit the name in Camera Name.

Check Display Name, Display Date and Display Week to show the information on the image.

Set the date format, time format, and display mode.

OSD Configuration Interface

Use the mouse to click and drag the text frame on the preview window to adjust the OSD position.

Click Apply.

## Configure Privacy Mask

Purpose

The privacy mask protects personal privacy by concealing parts of the image from view or recording with a masked area.

Go to Camera >Privacy Mask.

Select the camera to set privacy mask.

Click Enable to enable this feature.

Use the mouse to draw a zone on the window. The zones will be marked by different frame colors.

Privacy Mask Settings Interface

Up to 4 privacy masks zones can be configured and the size of each area can be adjusted.

Related Operation:

Clear the configured privacy mask zones on the window by clicking the corresponding Clear Zone1-4 icons on the right of the window, or click Clear All to clear all zones.

Click Apply.

## Configure the Image Parameters

Purpose

You can customize the image parameters including the brightness, contrast, and saturation for the Live View and recording effect.

Go to Camera>Display > Image Settings.

Select a camera from the drop-down list.

Adjust the slider or click on the up/down arrow to set the value of the brightness, contrast, or saturation.

Click Apply.

## Configure the Day/Night Switch

The camera can be set to day, night, or auto switch mode according to the surrounding illumination conditions.

Go to Camera>Display > Day/Night Switch.

Select the camera from the drop-down list.

Set the day/night switch mode to Day, Night, Auto, or Auto-Switch.

Auto: The camera automatically switches between day mode and night mode according to the illumination.

The sensitivity ranges from 0 to 7, and higher sensitivity more easily triggers the mode switch.

The switch time refers to the interval time between the day/night switch. You can set it from 5 sec to 120 sec.

Auto-Switch: The camera switches the day mode and the night mode according to the start time and end time you set.

Click the Apply.

## Configure Other Camera Parameters

For a connected camera, you can configure the camera parameters including the exposure mode, backlight and image enhancement.

Go to Camera>Display.

Select a camera from the drop-down list.

Configure the camera parameters.

- Exposure: Set the camera exposure time (1/10000 to 1 sec). A larger exposure value results in a brighter image.

- Backlight: Set the camera’s wide dynamic range (0 to 100). When the surrounding illumination and the object have large differences in brightness, you should set the WDR value.

- Image Enhancement: For optimized image contrast enhancement.

Click Apply.

# Live View

Live View displays the video image getting from each camera in real time.

## Start Live View

Click  on the main menu bar to enter the Live View.

          - Select a window and double click a camera from the list to play the video from the camera in the selected window.

          - Use the toolbar at the playing window bottom to realize the capture, instant playback, audio on/off, digital zoom, live view strategy, show information and start/stop recording, etc.

### Digital Zoom

Digital Zoom zooms into the live image in different magnifications (1x to 16x).

In the Live View mode, click  from the toolbar to enter the digital zoom interface.

Move the sliding bar or scroll the mouse wheel to zoom in/out the image to different magnifications (1x to 16x).

Digital Zoom

### Fisheye View

The device supports the fisheye camera expansion in Live View or playback mode.

- The fisheye expansion view feature is supported only by the DS-7600/7700/9600-I (/P) Series.

- The connected camera must support the fisheye view.

In the Live View mode, click  to enter the fisheye expansion mode.

Select the expansion view mode.

  - 180° Panorama (): Switch the Live View image to the 180° panorama view.

  - 360° Panorama (): Switch the Live View image to the 360° panorama view.

  - PTZ Expansion (): The PTZ Expansion is the close-up view of some defined area in the fisheye view or panorama expansion. It supports the electronic PTZ function, also called e-PTZ.

  - Radial Expansion (): In radial expansion mode, the whole wide-angle view of the fisheye camera is displayed. This view mode is called Fisheye View because it approximates the vision of a fish’s convex eye. The lens produces curvilinear images of a large area, while distorting the perspective and angles of objects in the image.

### 3D Positioning

3D Positioning (for I series device) zooms in/out of a specific live image area.

In Live View mode, click the  to enter the 3D positioning mode.

Zoom in/out of the image.

- Zoom In

Use the left mouse key to click on the desired position in the video image and drag a rectangle area in the lower right direction to zoom in.

- Zoom Out

Use the left mouse key to drag a rectangle area in the upper left direction to move the position to the center and enable the rectangle area to zoom out.

### Live View Strategy

In Live View mode, click  to enter the digital zoom operation interface in full screen mode.

Select the Live View strategy to Real-time, Balanced or Fluency.

## Target Detection

In Live View mode, the target detection function can detect a human motoion/face/vechicle/human body during the last 5 seconds and the following 10 seconds.

In Live View mode, click Target Detection to enter the target detection interface.

Check the checkbox to select different detection types: motion detection (), vehicle detection (), face detection (), and human body detection ().

Select the historical analysis () or real-time analysis () to obtain the results.

Target Detection

The smart analysis results of the detection are displayed in the list. Optionally, click a result in list to play the related video.

## Configure Live View Settings

Live View settings can be customized. You can configure the output interface, dwell time for screen to be shown, mute or turning on the audio, the screen number for each channel, etc.

Go to System > Live View > General.

Live View-General

Configure the Live View parameters.

Video Output Interface: Select the video output to configure.

Live View Mode: Select the display mode for Live View, e.g., 2*2, 1*5, etc.

Dwell Time: The time in seconds to wait between switching of cameras when using auto-switch in Live View.

Enable Audio Output: Enable/disable audio output for the selected video output.

Volume: Adjust the Live View volume, playback and two-way audio for the selected output interface.

Event Output: Select the output to show event video.

Full Screen Monitoring Dwell Time: Set the time in seconds to show alarm event screen.

Click OK.

## Configure Live View Layout

### Configure Custom Live View Layout

Go to System > Live View > View.

Click Set Custom Layout.

Click  on the Custom Layout Configuration interface.

Edit the layout name.

Select a window division mode from the toolbar.

Configure Live View Layout

Select multiple windows and click  to joint the windows. The selected windows must be in rectangle area.

Click Save.

Result:

The successfully configured view layout is displayed in the list.

Related Operations:

- Select a live view layout from the list and click  to edit the name.

- Select a live view layout from the list and click  to delete the name.

### Configure Live View Mode

Go to System > Live View > View

Select the video output interface.

Select a constant window-division layout or custom layout from the toolbar.

Select a division window, and double-click on a camera in the list to link the camera to the window.

You can enter the number in the text field to quickly search the camera from the list.

You can also click-and-drag the camera to the desired window on the Live View interface to set the camera order.

Click Apply.

Related Operations:

- Click  to start Live View for all channels.

- Click  to stop all Live View channels.

## Configure Camera Auto-Switch

You can set the camera’s auto-switch to play in different display modes.

Go to System > Live View > General.

Set the video output interface, Live View mode and dwell time.

- Video Output Interface: Select the video output interface.

- Live View Mode: Select the display mode for Live View, e.g., 2*2, 1*5, etc.

- Dwell Time: The time in seconds to wait between switching of cameras when in auto-switch. The range is from 5s to 300s.

Go to View Settings to set the view layout.

Click OK.

## Configure Channel-Zero Encoding

Purpose

Enable the channel-zero encoding when you need to get a remote view of many channels in real time from a web browser or CMS (Client Management System) software, in order to decrease the bandwidth requirement without affecting the image quality.

Go to System>Live View>General.

Set the video output interface to Channel-Zero.

Go to System>Live View>Channel-Zero.

Check Enable Channel-Zero Encoding.

Live View, Channel-Zero Encoding

Configure the Frame Rate, Max. Bitrate Mode, and Max. Bitrate. The higher frame rate and bitrate settings result in higher bandwidth requirement.

Click Apply.

Result:

You can view all of the channels on one screen using the CMS or a web browser.

# PTZ Control

## PTZ Control Wizard

Before You Start

Make sure the connected IP camera supports the PTZ function and is properly connected.

Purpose

Follow the PTZ Control Wizard to guide you through the basic PTZ operation.

Click  on the quick settings toolbar of the PTZ camera live view. The PTZ control wizard pops up as below.

PTZ Control Wizard

Follow the PTZ Control Wizard to adjust the PTZ view, focus, and zoom in/out.

(Optional) Check Do not show this prompt again.

Click OK.

## ConfigurePTZ Parameters

Purpose

Follow these procedures to set the PTZ parameters. The PTZ parameters configuration must be done before you can control the PTZ camera.

Click  on the quick settings toolbar of the PTZ camera’s Live View. The PTZ control panel displays on the right of the interface.

Click PTZ Parameters Settings to set the PTZ parameters.

PTZ Parameters Settings

Edit the PTZ camera parameters.

All the parameters should be exactly match the PTZ camera parameters.

Click OK to save the settings.

## Set PTZ Presets, Patrols, and Patterns

Before You Start

Make sure that the presets, patrols, and patterns are supported by PTZ protocols.

### Set Presets

Purpose

Follow these steps to set the preset location that you want the PTZ camera to point to when an event takes place.

Click  on the quick settings toolbar of the PTZ camera’s live view.

The PTZ control panel displays on the right of the interface.

Use the directional buttons on the PTZ control panel to wheel the camera to the location where you want to set a preset, and the zoom and focus operations can be recorded in the preset as well.

Click  in the lower right corner of Live View to set the preset.

Set Preset

Select the preset No. (1 to 255) from the drop-down list.

Enter the preset name in the text field.

Click Apply to save the preset.

Repeat steps 2-6 to save more presets.

(Optional) Click Cancel to cancel the location information of the preset.

(Optional) Click  in the lower right corner of Live View to view the configured presets.

View the Configured Presets

### Call Presets

Purpose

A presets enables the camera to point to a specified position such as a window when an event takes place.

Click  on the quick settings toolbar of the PTZ camera Live View.

Click  in the lower right corner of Live View.

Select the preset No. from the drop-down list.

Click Call to call it, or click  in the lower right corner of Live View, and click the configured preset to call it.

Call Preset (1)

Call Preset (2)

### Set Patrols

Purpose

Patrols can be set to move the PTZ to key points and have it stay there for a set duration before moving on to the next key point. The key points are correspond to the presets.

Click  on the quick settings toolbar of the PTZ camera’s Live View.

The PTZ control panel displays on the right of the interface.

Click Patrol to configure patrol.

Patrol Configuration

Select the patrol No. in the text field.

Click Set to enter the Patrol Settings interface.

Patrol Settings

Click  to add a key point to the patrol.

Key Point Configuration

- Configure key point parameters.

Preset: Determines the order the PTZ will follow while cycling through the patrol.

Speed: Defines the speed the PTZ will move from one key point to the next.

Duration: Refers to the duration to stay at the corresponding key point.

- Click Apply to save the key points to the patrol.

(Optional) Click  to edit the added key point.

Edit Key Point

(Optional) Select a key point and click  to delete it.

(Optional) Click  or  to adjust the key point order.

Click Apply to save the patrol settings.

Repeat steps 3-9 to set more patrols.

### Call a Patrol

Purpose

Calling a patrol makes the PTZ move according to the predefined patrol path.

          - Click  on the quick settings toolbar of the PTZ camera’s Live View.

The PTZ control panel displays on the right of the interface.

          - Click Patrol on the PTZ control panel.

Patrol Configuration

Select a patrol in the text field.

Click Call to start the patrol.

(Optional) Click Stop to stop the patrol.

### Set a Pattern

Purpose

Patterns can be set by recording the movement of the PTZ. You can call the pattern to make the PTZ move according to the predefined path.

          - Click  on the quick settings toolbar of the PTZ camera’s Live View.

The PTZ control panel displays on the right of the interface.

Click Pattern to configure a pattern.

Pattern Configuration

Select the pattern No. in the text field.

Set the pattern.

- Click Record to start recording.

- Click corresponding buttons on the control panel to move the PTZ camera.

- Click Stop to stop recording. The PTZ movement is recorded as the pattern.

Repeat steps 3-4 to set more patterns.

### Call a Pattern

Purpose

Follow the procedure to move the PTZ camera according to the predefined patterns.

          - Click  on the quick settings toolbar of the PTZ camera’s Live View.

          - The PTZ control panel displays on the right of the interface.

Click Pattern to configure pattern.

Pattern Configuration

Select a pattern in the text field.

Click Call to start the pattern.

(Optional) Click Stop to stop the pattern.

### Set Linear Scan Limits

Before You Start

Make sure the connected IP camera supports the PTZ function and is properly connected.

Purpose

Linear Scan trigger a scan in the horizontal direction in the predefined range.

This function is supported only by some certain models.

          - Click  on the quick settings toolbar of the PTZ camera’s Live View.

          - The PTZ control panel displays on the right of the interface.

Click the directional buttons to wheel the camera to the location of where you want to set the limit, and click Left Limit or Right Limit to link the location to the corresponding limit.

The speed dome linear scans from the left limit to the right limit, and you must set the left limit on the left side of the right limit. Also, the angle from the left limit to the right limit must be no more greater than 180º.

### Call Linear Scan

Before operating this function, make sure the connected camera supports the linear scan and is in HIKVISION protocol.

Purpose

Follow the procedure to call the linear scan in the predefined scan range.

          - Click  on the quick settings toolbar of the PTZ camera’s Live View.

          - The PTZ control panel displays on the right of the interface.

Click Linear Scan to start the linear scan and click it again to stop it.

(Optional) Click Restore to clear the defined left limit and right limit data.

Reboot the camera to have the settings take effect.

### One-Touch Park

Before operating this function, make sure the connected camera supports linear scan and is in HIKVISION protocol.

Purpose

Certain speed dome models can be configured to start a predefined park action (scan, preset, patrol and etc.) automatically after a period of inactivity (park time).

          - Click  on the quick settings toolbar of the PTZ camera’s Live View.

The PTZ control panel displays on the right of the interface.

Click Park (Quick Patrol), Park (Patrol 1), or Park (Preset 1) to activate the park action.

Park (Quick Patrol): The dome starts patrolling from the predefined preset 1 to preset 32 in order after the park time. Undefined presets will be skipped.

Park (Patrol 1): The dome starts moving according to the predefined patrol 1 path after the park time.

Park (Preset 1): The dome moves to the predefined preset 1 location after the park time.

The park time can be set only via the speed dome configuration interface. The default value is 5s by default.

Click Stop Park (Quick Patrol), Stop Park (Patrol 1), or Stop Park (Preset 1) to inactivate it.

## Auxiliary Functions

Before You Start

Make sure the connected IP camera supports the PTZ function and is properly connected.

Purpose

You can operate the auxiliary functions including light, wiper, 3D positioning, and center on the PTZ control panel.

          - Click  on the quick settings toolbar of the PTZ camera’s Live View.

          - The PTZ control panel displays on the right of the interface.

Click Aux Function.

Aux Function Configuration

Click the icons to operate the aux functions. See the table for the icon descriptions.

Description of Aux Functions Icons

| Icon | Description |
| --- | --- |
|  | Light on/off |
|  | Wiper on/off |
|  | 3D positioning |
|  | Center |

# Storage

## Storage Device Management

### Install the HDD

Before starting the device, install and connect an HDD to the device. Refer to the Quick Start Guide for the installation instructions.

### Add the Network Disks

You can add the allocated NAS or IP SAN disk to the device, and use it as a network HDD. Up to 8 network disks can be added.

Adding a NAS

Go to Storage > Storage Device.

Click Add to enter the Custom Add interface.

Select NetHDD from the drop-down list.

Set the type to NAS.

Enter the NetHDD IP address in the text field.

Click Search to search the available NAS disks.

Add NAS Disk

Select the NAS disk from the list shown below, or manually enter the directory in the NetHDD Directory text field.

Click the OK to complete the adding of the NAS disk.

Result:

After successfully adding the NAS disk, return to the HDD Information menu. The added NetHDD will be displayed in the list.

Adding an IP SAN

          - Go to Storage > Storage Device.

          - Click Add to enter the Custom Add interface.

          - Select NetHDD from the drop-down list.

          - Select the type to IP SAN.

          - Enter the NetHDD IP address in the text field.

          - Click Search to search the available IP SAN disks.

          - Select the IP SAN disk from the list.

          - Click OK to complete adding IP SAN disk.

A single IP SAN disk can be added.

Add IP SAN Disk

          - After having successfully added the IP SAN disk, return to the HDD Information menu. The added NetHDD will be displayed in the list.

If the installed HDD or NetHDD is uninitialized, select it and click Init for initialization.

### Configure eSATA for Data Storage

When there is an external eSATA device connected to the device, you can configure eSATA for the data storage, and you can manage the eSATA in the device.

Click Storage>Advanced.

Select the eSATA type to Export or Record/Capture from eSATA.

Export: Use the eSATA for backup.

Record/Capture: Use the eSATA for record/capture. Refer to the following steps for operating instructions.

Set eSATA Mode

When the eSATA type is set to Record/Capture, enter the storage device interface.

Edit the property of the selected eSATA, or initialize it as required.

## Storage Mode

### Configure HDD Groups

Purpose

Multiple HDDs can be managed in groups. Video from specified channels can be recorded onto a particular HDD group through HDD settings.

Go to Storage> Storage Device.

Check the checkbox to select the HDD to set the group.

Storage Device

Click  to enter the Local HDD Settings interface.

Local HDD Settings

Select the Group number for the current HDD.

Click OK.

Regroup the cameras for HDD if the HDD group number is changed.

Go to Storage> Storage Mode.

Check Group tab.

Select the group No. from the list.

Check the checkbox to select the IP camera(s) to record/capture on the HDD group.

Storage Mode-HDD Group

Click Apply.

Reboot the device to activate the new storage mode settings.

### Configure HDD Quota

Purpose

Each camera can be configured with an allocated quota for storing recorded files or captured pictures.

          - Go to Storage> Storage Mode.

Check the checkbox of Quota tab.

Select a camera to set quota.

Enter the storage capacity in the text fields of Max. Record Capacity (GB) and Max. Picture Capacity (GB).

Storage Mode-HDD Quota

(Optional) You can click Copy to if you want to copy the quota settings of the current camera to other cameras.

Click Apply.

When the quota capacity is set to 0, all cameras will use the total capacity of HDD for record and picture capture.

Reboot the device to activate the new storage mode settings.

## Recording Parameters

### Main Stream

The Main Stream refers to the primary stream that affects data recorded to the hard disk drive and will directly determine your recording quality and image size.

Comparing with the sub-stream, the main stream can provide a higher quality video with higher resolution and frame rate.

Frame Rate (FPS - Frames Per Second): refers to how many frames are captured each second. A higher frame rate is advantageous when there is movement in the video stream, as it maintains image quality throughout.

Resolution: Image resolution is a measure of how much detail a digital image can hold: the greater the resolution, the greater the level of detail. Resolution can be specified as the number of pixel-columns (width) by the number of pixel-rows (height), e.g.,1024×768.

Bitrate: The bit rate (in kbit/s or Mbit/s) is often referred to as speed, but actually defines the number of bits/time unit and not distance/time unit.

Enable H.264+ Mode: The H.264+ mode helps to ensure the high video quality with a lowered bitrate. It can effectively reduces the need of bandwith and HDD storage space.

A higher resolution, frame rate and bitrate setting will provide you the better video quality, but it will also require more internet bandwidth and use more storage space on the hard disk drive.

### Sub-Stream

The Sub-stream is a second codec that runs alongside the mainstream. It allows you to reduce the outgoing internet bandwidth without sacrificing your direct recording quality.

The Sub-stream is often exclusively used by smartphone applications to view live video. Users with limited internet speeds may benefit most from this setting.

### Picture

The picture refers to the live picture capture in continuous or event recording type. (Storage > Capture Schedule > Advanced)

Picture Quality: set the picture quality to low, medium or high. The higher picture quality results in more storage space requirement.

Interval: the interval of capturing live picture.

Capture Delay Time: the duration of capturing pictures.

### ANR

ANR (Automatic Network Replenishment) function which enables the IP camera to save the recording files in the local storage when the network is disconnected, and when the network is resumed, it uploads the files to the device.

Enable the ANR (Automatic Network Replenishment) function via the web browser (Configuration > Storage > Schedule Settings > Advanced).

### Configure Advanced Recording Settings

Go to Storage > Schedule Settings > Record Schedule/Capture Schedule.

Check Enable to enable scheduled recording.

Click Advanced to set the recording parameters.

Advanced Record Settings

Record Audio: Check the checkbox to enable or disable audio recording.

Pre-record: The time you set to record before the scheduled time or event. For example, when an alarm triggers the recording at 10:00, and if you set the pre-record time as 5 seconds, the camera records at 9:59:55.

Post-record: The time you set to record after the event or the scheduled time. For example, when an alarm triggered recording ends at 11:00, and if you set the post-record time as 5 seconds, it records till 11:00:05.

Expired Time: The expired time is period for a recorded file to be kept in the HDD. When the deadline is reached, the file will be deleted. If you set the expired time to 0, the file will not be deleted. The actual keeping time for the file should be determined by the capacity of the HDD.

Redundant Record/Capture: By enabling redundant record or capture you save the record and captured picture in the redundant HDD. See Chapter Configure Redundant Recording and Capture.

Stream Type: Main stream and sub-stream are selectable for recording. When you select sub-stream, you can record for a longer time with the same storage space.

Click OK to save the settings.

## Configure Recording Schedule

Set the record schedule, and then the camera automatically starts/stops recording according to the configured schedule.

Before you start

Make sure you have installed the HDDs to the device or added the network disks before you want to store the video files, pictures and log files.

Refer to the Quick Start Guide for the HDD installation.

Refer to Chapter 7.1.2 Add the Network Disk for network HDD connections.

Go to Storage > Recording Schedule.

Select a camera.

Check the Enable Schedule.

Select a Record Type. The record type can be Continuous, Motion Detection, Alarm, Motion | Alarm, Motion & Alarm, and Event.

Different recording types are configurable.

Continuous: scheduled recording.

Event: recording triggered by all event triggered alarm.

Motion: recording triggered by motion detection.

Alarm: recording triggered by alarm.

M/A: recording triggered by either motion detection or alarm.

M&A: recording triggered by motion detection and alarm.

POS: recording triggered by POS and alarm.

Select a day and click-and-drag the mouse on the time bar to set the record schedule.

Record Schedule

Repeat the above steps to schedule recording or capture for other days in the week.

The all-day continuous recording is configured for the device by factory default.

(Optional) Copy the schedule settings of the one day to the other days of the week or holiday.

- Click the  tab.

- Select the day (s) to duplicate with the same schedule settings.

- Click OK.

Copy Schedule to Other Days

Click Apply.

To enable Motion, Alarm, M | A (motion or alarm), M & A (motion and alarm) and Event triggered recording and capture, you must configure the motion detection settings, alarm input settings and other events as well. Please refer to Chapter 11 Event and Alarm Settings and Chapter 12 VCA Event Alarm for details for details.

## Configure Continuous Recording

Go to Camera > Encoding Parameters > Recording Parameters.

Set the continuous main stream/sub-stream recording parameters for the camera.

Go to Storage > Recording Schedule.

Select the recording type to Continuous.

Drag the mouse on the time bar to set the continuous recording schedule. Refer to Chapter 7.4 Configure Recording Schedule for details.

## Configure Motion Detection Triggered Recording

You can configure the recording triggered by the motion detection event.

Go to System > Event > Normal Event > Motion Detection.

Configure the motion detection and select the channel (s) to trigger the recording when motion event occurs. Refer to Chapter 11.3 Configure Motion Detection Alarm for details.

Go to Camera > Encoding Parameters > Recording Parameters.

Set the event main stream/sub-stream recording parameters for the camera.

Go to Storage > Recording Schedule.

Select the recording type to Motion.

Drag the mouse on the time bar to set the motion detection recording schedule. Refer to Chapter 7.4 Configure Recording Schedule for details.

## Configure Event Triggered Recording

You can configure the recording triggered by the motion detection, motion detection and alarm, face detection, vehicle detection, line crossing detection, etc.

Go to System > Event.

Configure the event detection and select the channel (s) to trigger the recording when event occurs. Refer to Chapter 11 Event and Alarm Settings and Chapter 12 VCA Event Alarm for details.

Go to Camera > Encoding Parameters > Recording Parameters.

Set the event main stream/sub-stream recording parameters for the camera.

Go to Storage > Recording Schedule.

Select the recording type to Event.

Drag the mouse on the time bar to set the event detection recording schedule. Refer to Chapter 7.4 Configure Recording Schedule for details.

## Configure Alarm Triggered Recording

You can configure the recording triggered by the motion detection, face detection, vehicle detection, line crossing detection, etc.

Go to System > Event > Normal Event > Alarm Input.

Configure the alarm input and select the channel (s) to trigger the recording when alarm occurs.

Refer to Chapter 11 Event and Alarm Settings and Chapter 12 VCA Event Alarm for details for details.

Go to Camera > Encoding Parameters > Recording Parameters.

Set the event main stream/sub-stream recording parameters for the camera.

Go to Storage > Recording Schedule.

Select the recording type to Alarm

Drag the mouse on the time bar to set the alarm recording schedule. Refer to Chapter 7.4 Configure Recording Schedule for details.

## Configure POS Event Triggered Recording

You can configure the recording triggered by the connected POS event, such as the transaction, etc.

Go to System >POS Settings.

Configure the POS and select the channel (s) in the Event Linkage to trigger the recording when POS event occurs.

Refer to Chapter 13 Smart Analysis for details.

Go to Camera > Encoding Parameters > Recording Parameters.

Set the event main stream/sub-stream recording parameters for the camera.

Go to Storage > Recording Schedule.

Select the record type to POS Event.

Set the schedule for the POS event triggered recording. Refer to Chapter 7.4 Configure Recording Schedule for details.

## Configure Picture Capture

The picture refers to the live picture capture in continuous or event recording type.

Go to Storage > Capture Schedule > Advanced.

Set the picture parameters.

Resolution: set the resolution of the picture to capture.

Picture Quality: set the picture quality to low, medium or high. The higher picture quality results in more storage space requirement.

Interval: the interval of capturing live picture.

Capture Delay Time: the duration of capturing pictures.

Go to Storage > Capture Schedule.

Select the camera to configure the picture capture.

Set the picture capture schedule. Refer to Chapter 7.4 Configure Recording Schedule for details.

## Configure Holiday Recording and Capture

Purpose:

Follow the steps to configure the record or capture schedule on holiday for that year. You may want to have different plan for recording and capture on holiday.

Go to System > Holiday Settings.

Select a holiday item from the list and click.

Check the Enable to configure the holiday.

Edit Holiday Settings

- Edit the holiday name.

- Select the mode to by date, by week or by month.

- Set the start and end date of the holiday.

- Click OK.

Set the schedule for the holiday recording. Refer to Chapter 7.4 Configure Recording Schedule for details.

## Configure Redundant Recording and Capture

Purpose:

Enabling redundant recording and capture, which means saving the record files and captured pictures not only in the R/W HDD but also in the redundant HDD, will effectively enhance the data safety and reliability. .

You must set the storage mode to Group before you set the HDD property to Redundancy. For detailed information, please refer to Chapter 7.2.1 Configure HDD Group. There should be at least another HDD which is in Read/Write status.

Go to Storage > Storage Device.

Select a HDD from the list and Click  to enter the Local HDD Settings interface.

Set the HDD property to Redundancy.

HDD Property-Redundancy

Go to Storage > Schedule Settings > Record Schedule/Capture Schedule.

Click Advanced to set the camera recording parameters.

Record Parameters

Check the checkbox of Redundant Record/Capture.

Click OK to save settings.

# Disk Array (RAID)

Purpose

A disk array is a data storage virtualization technology that combines multiple physical disk drives into a single logical unit. Also known as a “RAID”, an array stores data over multiple HDDs to provide enough redundancy so that data can be recovered if one disk fails. Data is distributed across the drives in one of several ways called "RAID levels", based the redundancy and performance required.

Disk arrays are supported by DS-9600NI-I Series device only.

## Create a Disk Array

Purpose

The device supports software-based disk arrays. Enable the RAID function as required. Two ways are available for creating an array: one-touch configuration and manual configuration. The following flow chart shows the process of creating array.

### Enable a RAID

Purpose

Perform the following steps to enable the disk array function.

Go to Storage > Advanced.

Advanced

Check Enable RAID.

Click Apply.

Reboot the device to have settings take effect.

### One-Touch Creation

Purpose

One-touch configuration creates the disk array. By default, the array type created by one-touch configuration is RAID 5.

Before You Start

Enable the RAID function. For details, refer to Chapter 8.1.1 Enable a RAID.

Install at least 3 HDDs. If more than 10 HDDs are installed, 2 arrays will be created. To maintain reliability and stability running of the HDDs, it is recommended to use of enterprise-level HDDs of the same model and capacity.

Go to Storage > RAID Setup > Physical Disk.

Physical Disk

Click One-touch Config.

Edit the array name in Array Name and click OK to start configuring.

If you install 4 or more HDDs, a hot spare disk for array rebuilding will be created.

When a message box pops up when the array creation is completed, click OK on it.

Optionally, the device will automatically initialize the created array. Go to Storage > RAID Setup > Array to view the information of the created arrray.

### Manual Creation

Purpose

Manually create a RAID 0, RAID 1, RAID 5, RAID 6, or RAID 10 array.

          - Go to Storage > RAID Setup > Physical Disk.

Click Create.

Create Array Window

Input the array name.

Select RAID Level as RAID 0, RAID 1, RAID 5, RAID 6, or RAID 10 as required.

Select the physical disks to constitute the array.

Required Number of HDDs

| RAID Level | Required Number of HDDs |
| --- | --- |
| RAID 0 | At least 2 HDDs. |
| RAID 1 | At least 2 HDDs. |
| RAID 5 | At least 3 HDDs. |
| RAID 6 | At least 4 HDDs. |
| RAID 10 | The number of HDD must be an even ranges from 4 to 16. |

Click OK.

Optionally, the device will automatically initialize the created array. Go to Storage > RAID Setup > Array to view the information of the created arrray.

Array List

## Rebuild an Array

Purpose:

The array status includes Functional, Degraded, and Offline. To ensure the high security and reliability of the data stored in an array, take immediate and proper maintenance of the arrays according its status.

Functional: No disk loss in the array.

Offline: The number of lost disks has exceeded the limit.

Degraded: If any HDD fails in the array, the array degrades. Restore it to Functional status by rebuilding the array.

### Configure a Hot Spare Disk

Purpose

Hot spare disks are required for disk array automatic rebuilding.

Go to Storage > RAID Setup > Physical Disk.

Physical Disk

Click  of an available HDD to set it as the hot spare disk.

### Automatically Rebuild an Array

Purpose

The device can automatically rebuild degraded arrays with the hot spare disks.

Before You Start

Create hot spare disks. For details, refer to Chapter 8.2.1 Configure a Hot Spare Disk.

The device will automatically rebuild degraded arrays with the hot spare disks. Go to Storage > RAID Setup > Array to view rebuilding progress.

Array List

### Manually Rebuild an Array

Purpose

If no hot spare disks are configured, rebuild a degraded array manually.

Before You Start

At least one available physical disk must exist to rebuild an array.

          - Go to Storage > RAID Setup > Array.

Array List

Click  of the degraded array.

Rebuild Array

Select the available physical disk.

Click OK.

Click OK on the pop up message box “Do not unplug the physical disk when it is under rebuilding.”

## Delete an Array

Deleting an array will delete all the data saved to it.

Go to Storage > RAID Setup > Array.

Array List

Click  of the array to delete it.

Attention

Click Yes on the popup message box.

## Check and Edit Firmware

Purpose

You can view the firmware information and set the background task speed on the Firmware interface.

Go to Storage > RAID Setup > Firmware.

Firmware

Optionally, set the Background Task Speed.

Click Apply.

# File Management

## Search and Export All Files

### Search Files

Purpose

Specify detailed conditions to search videos and pictures.

Go to File Management > All Files.

Specify detailed conditions, including time, camera, event type, etc.

Search All Files

Click Search to display results. The matched files will be displayed.

### Export Files

Purpose

Export files for backup purposes using a USB device (USB flash drive, USB HDD, USB optical disc drive), SATA optical disc drive, or eSATA HDD.

Search files to export. For details, see 9.1.1 Search Files.

Click files to select and click Export.

Select the file to export as Video and Log and click OK.

Click OK to export files to backup device.

## Search and Export Human Files

### Search Human Files

Purpose

Specify detailed conditions by which to search human pictures and videos.

Before You Start

Configure the human body detection function for the cameras you want to search and export human pictures and videos.

Go to File Management > Human Files.

Select Time and Camera to search.

Search Human Files

Click Search to display results. The matched files are displayed in thumbnails or a list.

Select Target Picture or Source Picture in the menu bar to display related pictures only.

Target Picture: Display the search results of people close-ups.

Source Picture: Display the search results of original pictures captured by the camera.

### Export Human Files

Purpose

Export files for backup purposes using a USB device (USB flash drive, USB HDD, USB optical disc drive), SATA optical disc drive, or eSATA HDD.

Search for the human files to export. For details, see 9.2.1 Search Human Files.

Click to select files and click Export.

Select the file to export as Video and Log and click OK.

Click OK to export files to backup device.

## Search and Export Vehicle Files

### Search Vehicle Files

Purpose

Specify detailed conditions by which to search vehicle pictures and videos.

Before You Start

Configure the vehicle detection function for the cameras you want to search and export vehicle pictures and videos.

Go to File Management > Vehicle Files.

Specify detailed conditions, including Time, Camera, Plate No., and Area/Country.

Search Vehicle Files

Click Search to display results. The matched files are displayed in thumbnails or a list.

Select Target Picture or Source Picture in the menu bar to display related pictures only. Select Video or Picture to specify the file type.

Target Picture: Display the search results of vehicle close-ups.

Source Picture: Display the search results of original pictures captured by the camera.

### Export Vehicle Files

Purpose

Export files for backup purposes to a USB device (USB flash drive, USB HDD, USB optical disc drive), SATA optical disc drive, or eSATA HDD.

Search for the vehicle files to export. For details, see 9.3.1 Search Vehicle Files.

Click files to select and click Export.

Select the file to export as Video and Log and click OK.

Click OK to export files to backup device.

## Search History Operation

### Save Search Conditions

Purpose

You can save the search conditions for future reference and quick searches.

Go to File Management > All Files/People Appearance File/Vehicle File.

Set the search conditions.

Click Save.

Enter a name in text field and click Finished. The saved search conditions will be displayed in search history list.

### Call Search History

Purpose

You can quickly search files by calling the search history.

Go to File Management > All Files/Human Files/Vehicle Files.

Click a search conditon to search files quickly.

# Playback

## Play Video Files

### Instant Playback

Instant Playback enables the device to play the recorded video files recorded in the last five minutes. If no video is found, it means there is no recording during the last five minutes.

On the Live View window of the selected camera, move the cursor to the window bottom to access the toolbar.

Click  to start instant playback.

Playback Interface

### Play Normal Video

          - Go to Playback.

Check one or more cameras in the camera list to start playing the video.

Select a date in the calendar to start playing the video.

Use the toolbar in the bottom part of the playback interface to control the playing and perform a series of operations. Refer to Chapter 10.2 Playback Operations 8.2.

Click the channel(s) to execute simultaneous playback of multiple channels.

Playback Interface

256x playing speed is supported.

### Play Smart Searched Video

In smart playback mode, the device can analyze the video containing the motion, line, or intrusion detection information, mark it in red, and play the smart searched video.

The smart playback must be in the single-channel playing mode.

          - Go to Playback.

          - Start playing the video of camera.

          - Click Smart.

          - From the toolbar at the bottom of the playing window, click the motion/line crossing/ intrusion icon for search.

Playback by Smart Search

Set the rules and areas for smart search of line crossing detection, intrusion detection or motion detection event triggered recording.

- Line Crossing Detection

- Click the  icon.

- Click on the image to specify the start point and end point of the line.

- Intrusion Detection

- Click the  icon.

- Specify 4 points to set a quadrilateral region for intrusion detection. Only one region can be set.

- Motion Detection

- Click the  icon.

- Hold the mouse on the image to draw the detection area manually.

- Click Search  to search the matched video and start to play it.

### Play Custom Searched Files

You can play the files by custom search with different conditions.

          - Go to Playback.

          - Select a camera or cameras from the list.

          - Click Custom Search on the left bottom to enter the Search Condition interface.

          - Enter the search conditions for the files, e.g., time, file status, event type, etc.

Custom Search

          - Click Search.

Custom Searched Video Files

          - On the search results interface, select a file and click to start playing the video.

### Play Tag Files

Purpose

Video tag allows you to record related information such as people and locations of a certain time point during playback. You can use video tag(s) to search for video files and position time point.

Before playing back by tag:

Add Tag Files

Go to Playback.

Search and play back the video file(s).

Click  to add the tag.

Edit the tag information.

Click OK.

Max. 64 tags can be added to a single video file.

Edit Tag Files

You can edit the tag information for the existed tag video.

Go to Playback.

Click Tag.

The available tags are white marked and displayed in the time bar.

Point the white marked tag in the time bar to access the tag information.

Edit Tag Files

Click  to edit the tag name.

Click OK.

Play Tag Files

          - Go to Playback.

          - Click Custom Search on the left bottom to enter the Search Condition interface.

          - Enter the search conditions for the tag files, including the time and the tag keyword.

Tag Search

          - Click Search.

Searched Tag Files

          - On the search results interface, select a tag file and click to start playing the video.

### Play Event Files

Purpose

Play back video files on one or several channels searched by event type (e.g., alarm input, motion detection, line crossing detection, face detection, vehicle detection, etc.).

          - Go to Playback.

          - Click Custom Search on the left bottom to enter the Search Condition interface.

          - Enter the search conditions for the event files, e.g., time, event type, file status, vehicle information (for vehicle detection event), etc.

          - Click Search.

          - On the search results interface, select an event video file/picture file and double click to start playing the video.

Event Files

You can click  or  button to play 30s backward or forward.

Refer to Chapter 11

Event and Alarm Settings and Chapter 12 VCA Event Alarm for details for event and alarm settings.

Refer to Chapter 7.7 Configure Event Triggered Recording for the event triggered recording/capture settings.

### Play Video Synopsis

Purpose:

Video synopsis is an approach to create a short video summary of a long video. It tracks and analyzes moving objects (also called events), and converts video streams into a database of objects and activities.

Before you start:

Enable Dual-VCA and intrusion detection/line crossing detection on the network camera.

Go to Playback interface.

Click  in toolbar.

Synopsis Playback

Select a camera in channel list.

Specify Start Time and End Time. The duration must be within 24 hours.

Click Search to start play.

Optionally, double click a target on the playback window. A 60-second video of 30 seconds before and after the time will be played.

### Play by Sub-periods

Purpose:

The video files can be played in multiple sub-periods simultaneously on the screen.

Go to Playback.

Select  icon at the left bottom corner to enter the sub-period playing mode.

Select a camera.

Set the start time and end time for searching video.

Select the different multi-period at the right bottom corner, e.g., 4-Period.

According to the defined number of split-screens, the video files on the selected date can be divided into average segments for playback. E.g., if there are video files existing between 16:00 and 22:00, and the 6-screen display mode is selected, then it can play the video files for 1 hour on each screen simultaneously.

### Play Log Files

Purpose

Play back record file(s) associated with channels after searching system logs.

Go to Maintenance>Log Information.

Click Log Search.

Set search time and type and click Search.

System Log Search Interface

Choose a log with a video file and click  to start playing the log file.

### Play External Files

Purpose

You can play files from external storage devices.

Before You Start

Connect the storage device with the video files to your device.

Go to Playback.

Click  at the left bottom corner.

Select and click t  or double click to play the file.

## Playback Operations

### Set Play Strategy in Smart/Custom Mode

Purpose:

When you are in the smart or custom video playback mode, you can set the playing speed separately for the normal video and the smart/custom video, or you can select to skip the normal video.

In the Smart/Custom video playback mode, click  to set the play strategy.

- When Do not Play Normal Videos is checked, the device will skip the normal video and play the smart (motion/line crossing/intrusion) video and the custom (searched video) only in the normal speed (X1).

- When Do not Play Normal Videos is unchecked, you can set the play speed for the normal video the smart/custom video separately. The speed range is from X1 to XMAX.

You can set the speed in the single-channel play mode only.

Play Strategy

### Edit Video Clips

You can take video clips during playback and export the clips.

In the Video Playback mode, click  to start the video clipping operation.

- : Set the start time and end time of the video clipping.

- : Export the video clips to the local storage device.

### Switch between Main Stream and Sub-Stream

You can switch between the main stream and the sub-stream during playback.

: Play the video in main stream.

: Play the video in sub-stream.

The encoding parameters for the main stream and sub-stream can be configured in Storage > Encoding Parameters.

### Thumbnails View

With the thumbnails view on the playback interface, you can conveniently locate the required video files on the time bar.

In the playback mode, move the mouse to the time bar to get the preview thumbnails of the video files.

Thumbnails View

You can select and click on a thumbnail to enter the full-screen playback.

### Fisheye View

You can enter the fisheye expansion view during the video playback.

Click the  to enter the fisheye expansion mode.

  - 180° Panorama (): Switch the live view image to the 180° panorama view.

  - 360° Panorama (): Switch the Live View image to the 360° panorama view.

  - PTZ Expansion (): The PTZ Expansion is the close-up view of a defined area in the fisheye view or panorama expansion, and it supports the electronic PTZ function, which is also called e-PTZ.

  - Radial Expansion (): In the radial expansion mode, the whole wide-angle view of the fisheye camera is displayed. This view mode is called Fisheye View because it approximates the vision of a fish’s convex eye. The lens produces curvilinear images of a large area, while distorting the perspective and angles of objects in the image.

### Fast View

Hold the mouse to drag on the time bar to get a fast view of the video files.

In the Video Playback mode, hold and drag the mouse through the playing time bar to fast view the video files.

Release the mouse at the required time point to enter the full-screen playback.

### Digital Zoom

Digital zoom adopts encoding technology to enlarge the image which will result in image quality damage.

In the Video Playback mode, click  in the toolbar to enter the digital zoom interface.

Move the sliding bar or scroll the mouse wheel to zoom in/out of the image to different magnifications (1 to16X).

Digital Zoom

### POS Information Overlay

The device can be connected with the POS machine/server, and receive the transaction message for overlay on the image during playback.

In the video playback mode, click  to overlay the POS transaction information on the playback video.

When the playing speed is higher than 2x, the POS information cannot be overlaid on the video.

# Event and Alarm Settings

## Configure Arming Schedule

Select the Arming Schedule tab.

Choose a day of the week and set the time period. Up to eight time periods can be set each day.

Time periods cannot repeat or overlapped.

Set Arming Schedule

(Optional) To copy the same arming schedule of the current day to the other day (s) of the week or holiday, you can click  to copy the arming schedule settings.

Click Apply to save the settings.

## Configure Alarm Linkage Actions

Click Linkage Action to set the alarm linkage actions.

Set Linkage Actions

Select the normal linkage actions, trigger alarm output, or trigger the recording channel.

Full Screen Monitoring

When an alarm is triggered, the local monitor displays in full screen the video image from the alarming channel configured for full screen monitoring.

If alarms are triggered simultaneously in several channels, their full-screen images will be switched at an interval of 10 seconds (default dwell time). A different dwell time can be set by going to System>Live View > Full Screen Monitoring Dwell Time.

Auto-switch will terminate once the alarm stops and return to the Live View interface.

Select the channel(s) you want to trigger full screen monitoring in Trigger Channel settings.

Audible Warning

It will trigger an audible beep when an alarm is detected.

Notify Surveillance Center

It will send an exception or alarm signal to the remote alarm host when an event occurs. The alarm host refers to the PC installed with Remote Client.

The alarm signal will be transmitted automatically at detection mode when a remote alarm host is configured. Refer to Chapter 15.8 Configure Ports for alarm host configuration.

Send Email

It will send an e-mail with alarm information to the user when an alarm is detected.

Refer to 15.7 Configure Email for details of e-mail configuration details.

Check the checkbox to select the alarm output when an alarm is triggered.

To trigger an alarm output when an event occurs, please refer to Chapter 11.6.3 Configure Alarm Output to set the alarm output parameters.

Click Trigger Channel and select one or more channels that will record/capture or perform full-screen monitoring when a motion alarm is triggered.

You have to set the recording schedule to realize this function. Refer to Refer to Chapter 7.4 Configure Recording Schedule for setting the recording schedule.

Click Apply to save the settings.

## Configure Motion Detection Alarms

Motion Detection enables the device to detect the moving objects in the monitored area and trigger alarms.

Go to System> Event>Normal Event>Motion Detection.

Set Motion Detection

Select the camera to configure the motion detection.

Check Enable.

Set the motion detection area.

- Full screen: Click to set the full-screen motion detection for the image.

- Customized area: Click-and drag the mouse to click and drag on the preview screen to draw the customized motion detection area (s).

Click Clear to clear the current motion detection area settings and draw again.

Set sensitivity (0-100). The sensitivity allows you to calibrate how readily movement triggers the alarm. A higher value results in the more readily to triggers motion detection.

Set the arming schedule. Refer to Chapter 11.1 Configure Arming Schedule.

Set the linkage actions. Refer to Chapter 11.2 Configure Alarm Linkage Actions.

## Configure Video Loss Alarms

Purpose

Video Loss Detection detects video loss of a channel and takes alarm response action(s).

Go to System> Event>Normal Event>Video Loss.

Set Video Loss Detection

Select the camera to configure the video loss detection.

Check Enable.

Set the arming schedule. Refer to Chapter 11.1 Configure Arming Schedule.

Set the linkage actions. Refer to Chapter 11.2 Configure Alarm Linkage Actions.

## Configure Video Tampering Alarms

Purpose

Video Tampering Detection triggered an alarm when the camera lens is covered and takes alarm response action(s).

Go to System> Event>Normal Event>Video Tampering.

Select the camera to configure the video tampering detection.

Set Video Tampering Setting

Check Enable.

Set the video tampering area. Click-and-drag the mouse on the preview screen to draw the customized video tampering area.

Click Clear to clear the current area settings and draw again.

Set sensitivity level (0-2). 3 levels are available. The sensitivity calibrates how readily movement triggers the alarm. A higher value more readily triggers the video tampering detection.

Set the arming schedule. Refer to Chapter 11.1 Configure Arming Schedule.

Set the linkage actions. Refer to Chapter 11.2 Configure Alarm Linkage Actions.

## Configure Sensor Alarms

Purpose:

Set the handling action of an external sensor alarm.

### Configure Alarm Inputs

Go to System> Event>Normal Event>Alarm Input

Select an alarm input item from the list and click .

Alarm Input

Select the alarm input type to N.C or N.O.

Edit the alarm name.

Check Input.

Set the arming schedule. Refer to Chapter 11.1 Configure Arming Schedule.

Set the linkage actions. Refer to Chapter 11.2 Configure Alarm Linkage Actions.

### Configure One-Key Disarming

One-Key Disarming disarm Alarm Input 1 by one-key operation.

Go to System> Event>Normal Event>Alarm Input

Select Alarm Input 1 from the list and click .

Set the alarm input type to N.C or N.O.

Edit the alarm name.

Check Enable One-Key Disarming.

One-Key Alarm Disarming

Select the alarm linkage action(s) you want to disarm for the local Alarm Input.

When Alarm Input 1 (Local<-1) is enabled with one-key disarming, the other alarm input settings are not configurable.

Click Apply to save the settings.

### Configure Alarm Outputs

Trigger an alarm output when an alarm is triggered.

          - Go to System> Event>Normal Event>Alarm Output.

Select an alarm output item from the list and click .

Edit the alarm name.

Select the dwell time (the alarm duration) from 5s to 600s, or Manually Clear.

Manually Clear: You should manually clear the alarm when the alarm occurs. Refer to Chapter 11.9 Trigger or Clear Alarm Output Manually for detailed instructions.

Set the arming schedule. Refer to Chapter 11.1 Configure Arming Schedule.

Alarm Output

          - (Optional) Click Copy to copy the same settings to other alarm output (s).

## Configure Exceptions Alarms

Exception events can be configured to take the event hint in the Live View window and trigger alarm output and linkage actions.

Go to System> Event>Normal Event>Exception.

(Optional) Enable the event hint to display it in the live view window.

- Check Enable Event Hint.

- Click  to select the exception type (s) to take the event hint.

Event Hint Settings

Select the excetion type from the drop-down list to set the linkage actions.

Exceptions Handling

Set the normal linkage and alarm output triggering. Refer to Chapter 11.8 Setting Alarm Linkage Actions

## Setting Alarm Linkage Actions

Purpose

Alarm linkage actions will be activated when an alarm or exception occurs, including Event Hint Display, Full Screen Monitoring, Audible Warning (buzzer), Notify Surveillance Center, Trigger Alarm Output, and Send Email.

### Configure Auto-Switch Full Screen Monitoring

When an alarm is triggered, the local monitor displays in full screen the video image from the alarming channel configured for full screen monitoring. And when the alarm is triggered simultaneously in several channels, you must configure the auto-switch dwell time.

Go to System > View > General.

Set the event output and dwell time.

Event Output: Select the output to show the event video.

Full Screen Monitoring Dwell Time: Set the time in seconds to show the alarm event screen. If alarms are triggered simultaneously in several channels, their full-screen images will be switched at an interval of 10 seconds (default dwell time).

Go to the Linkage Action interface of the alarm detection (e.g., motion detection, video tampering, face detection, etc.).

Select the Full Screen Monitoring alarm linkage action.

Select the channel(s) in Trigger Channel settings you for make full screen monitoring in Trigger Channel Settings.

Auto-switch will terminate once the alarm stops and back to the live view interface.

### Configure Audio Warning

The audio warning has the system to trigger an audible beep when an alarm is detected.

Go to System>View>General.

Enable the audio output and set the volume.

Go to the Linkage Action interface of the alarm detection (e.g., motion detection, video tampering, face detection, etc.).

Select the Audio Warning alarm linkage action.

### Notify Surveillance Center

The device can send an exception or alarm signal to the remote alarm host when an event occurs. The alarm host refers to the PC installed with client software (e.g., iVMS-4200, iVMS-5200).

Go to System > Network > Advanced > More Settings.

Set the alarm host IP and alarm host port.

Go to the Linkage Action interface of the alarm detection (e.g., motion detection, video tampering, face detection, etc.).

Select the Notify Surveillance Center.

### Configure E-mail Linkage

The system can send an email with alarm information to a user or users when an alarm is detected.

Please refer to Chapter 15.7 Configure Email for details of Email configuration.

Go to System>Network>Advanced.

Configure the e-mail settings.

Go to the Linkage Action interface of the alarm detection (e.g., motion detection, video tampering, face detection, etc.).

Select the Send Email alarm linkage action.

### Trigger Alarm Outputs

The alarm output can be triggered by the alarm input, motion detection, video tampering detection, face detection, line crossing detection, and any all other events.

Go to the Linkage Action interface of the alarm detection (e.g., motion detection, face detection, line crossing detection, intrusion detection, etc.).

Click the Trigger Alarm Output tab.

Select the alarm output (s) to trigger.

          - Go to System> Event>Normal Event>Alarm Output.

Select an alarm output item from the list.

Refer to Chapter 11.6.3 Configure Alarm Output for the alarm output settings.

### Configure PTZ Linkage

The system can trigger the PTZ actions (e.g., call preset/patrol/pattern) when the alarm event, or VCA detection events occurs.

Make sure the connected PTZ or speed dome connected supports PTZ linkage.

Go to the Linkage Action interface of the alarm input or VCA detection (e.g., face detection, line crossing detection, intrusion detection, etc.).

Select the PTZ Linkage.

Select the camera to perform the PTZ actions.

Select the preset/patrol/pattern No. to call when the alarm events occur.

PTZ Linkage

You can set only one PTZ type for the linkage action each time.

## Trigger or Clear Alarm Output Manually

Purpose

Sensor alarm can be triggered or cleared manually. When the Manually Clear is selected for the dwell time of an alarm output, the alarm can be cleared only by clicking Clear button.

          - Go to System> Event>Normal Event>Alarm Output.

Select the alarm output you want to trigger or clear.

Click Trigger/Clear to trigger or clear an alarm output.

Alarm Output

# VCA Event Alarm

The device supports receiving VCA detections sent by connected IP cameras. Enable and configure VCA detection on the IP camera settings interface first.

VCA detections must be supported by the connected IP camera.

Refer to the network camera’s user manual for detailed VCA detection instructions.

## Face Detection

Purpose

The Face Detection function detects the face appearing in the surveillance scene. Linkage actions can be triggered when a human face is detected.

Go to System > Event > Smart Event.

Click Face Detection.

Face Detection

Select a Camera to configure.

Check Enable Face Detection.

Optionally, check Save VCA Picture to save the captured pictures of face detection.

Drag the Sensitivity slider to set the detection sensitivity. Sensitivity range: [1-5]. The higher the value is, the more easily the face will be detected.

Set the arming schedule. Refer to Chapter 11.1 Configure Arming Schedule.

Set the linkage actions. Refer to Chapter 11.2 Configure Alarm Linkage Actions.

Click Apply.

## Vehicle Detection

Purpose

Vehicle Detection is available for road traffic monitoring. In Vehicle Detection, a passed vehicle can be detected and the picture of its license plate can be captured. You can send an alarm signal to notify the surveillance center and upload the captured picture to an FTP server.

Go to System > Event > Smart Event.

Click Vehicle.

Vehicle Detection

Select a camera to configure.

Check Enable Vehicle Detection.

Optionally, check Save VCA Picture to save the captured vehicle detection pictures.

Set the arming schedule. Refer to Chapter 11.1 Configure Arming Schedule.

Set the linkage actions. Refer to Chapter 11.2 Configure Alarm Linkage Actions.

Configure rules, including Area Settings, Picture, Overlay Content, and Blacklist and Whitelist. Area Settings: Up to 4 lanes are selectable.

Click Save.

Refer to the Network Camera User Manual for detailed instructions for the vehicle detection.

## Line Crossing Detection

Purpose

Line crossing detection detects people, vehicles, and objects crossing a set virtual line. The detection direction can be set as bidirectional, from left to right or from right to left.

Go to System > Event > Smart Event.

Click Line Crossing.

Line Crossing Detection

Select a camera to configure.

Check the Enable Line Crossing Detection checkbox.

Optionally, check Save VCA Picture to save the captured pictures of line crossing detection pictures.

Follow the steps to set the line crossing detection rules and detection areas.

- Select an Arming Region to configure. Up to 4 arming regions are selectable.

Select the Direction as A<->B, A->B, or A<-B.

A<->B: Only the arrow on the B side shows. An object crossing a configured line in both directions can be detected and trigger alarms.

A->B: Only an object crossing the configured line from the A side to the B side can be detected.

B->A: Only an object crossing the configured line from the B side to the A side can be detected.

Drag the Sensitivity slider to set the detection sensitivity. Sensitivity range: sensitivity. The higher the value is, the more easily the detection alarm will be triggered.

Click Draw Region and set two points in the preview window to draw a virtual line.

Set the arming schedule. Refer to Chapter 11.1 Configure Arming Schedule.

Set the linkage actions. Refer to Chapter 11.2 Configure Alarm Linkage Actions.

Click Apply.

## Intrusion Detection

Purpose

The Intrusion Detection Function detects people, vehicles or other objects that enter and loiter in a pre-defined virtual region. Specific actions can be taken when an alarm is triggered.

Go to System > Event > Smart Event.

Click Intrusion.

Intrusion Detection

Select a camera to configure.

Check Enable Intrusion Detection.

Optionally, check Save VCA Picture to save the captured intrusion detection pictures.

Follow these steps to set the detection rules and detection areas.

- Select a Virtual Panel to configure. Up to 4 virtual panels are selectable.

Drag the sliders to set Time Threshold, Sensitivity, and Percentage.

Time Threshold: The time an object loiter in the region. When the duration of the object in the defined detection area exceeds the threshold, the device will trigger an alarm. Its range is [1s-10s].

Sensitivity: The size of the object that can trigger the alarm. The higher the value is, the more easily the detection alarm will be triggered. Its range is [1-100].

Percentage: The ratio of the in-region part of the object that can trigger the alarm. For example, if the percentage is 50%, when the object enters the region and occupies half of the whole region, the device will trigger an alarm. Its range is [1-100].

Click Draw Region and draw a quadrilateral in the preview window by specifying four vertices of the detection region.

Set the arming schedule. Refer to Chapter 11.1 Configure Arming Schedule.

Set the linkage actions. Refer to Chapter 11.2 Configure Alarm Linkage Actions.

Click Apply.

## Region Entrance Detection

Purpose

The Region Entrance Detection Function detects objects that enter a pre-defined virtual region.

Go to System Management > Event Settings > Smart Event.

Click the Region Entrance Detection item.

Region Entrance Detection

Select a camera to configure.

Check Enable Region Entrance Detection.

Optionally, check Save VCA Picture to save the captured pictures of region entrance detection pictures.

Follow thees steps to set the detection rules and detection areas.

- Select an Arming Region to configure. Up to 4 regions are selectable.

Drag the sliders to set Sensitivity.

Sensitivity: The higher the value is, the more easily the detection alarm will be triggered. Its range is [0-100].

Click Draw Region and draw a quadrilateral in the preview window by specifying four vertices of the detection region.

Configure Arming Schedule and Linkage Action.

Click Apply.

## Region Exiting Detection

Purpose

The Region Exiting Detection Function detects objects that exit from a pre-defined virtual region.

Go to System > Event > Smart Event.

Click Region Exiting.

Region Exiting Detection

Select a camera to configure.

Check Enable Region Exiting Detection.

Optionally, check Save VCA Picture to save the captured region exiting detection pictures.

Follow these steps to set the detection rules and detection areas.

- Select an Arming Region to configure. Up to 4 regions are selectable.

Drag the sliders to set Sensitivity.

Sensitivity: The higher the value is, the more easily the detection alarm will be triggered. Its range is [0-100].

Click Draw Region and draw a quadrilateral in the preview window by specifying four vertices of the detection region.

Set the arming schedule. Refer to Chapter 11.1 Configure Arming Schedule.

Set the linkage actions. Refer to Chapter 11.2 Configure Alarm Linkage Actions.

Click Apply.

## Unattended Baggage Detection

Purpose

The Unattended Baggage Detection Function detects the objects left over in a pre-defined region such as the baggage, purses, dangerous materials, etc., and a series of actions can be taken when the alarm is triggered.

Go to System > Event > Smart Event.

Click Unattended Baggage.

Unattended Baggage Detection

Select a camera to configure.

Check Enable Unattended Baggage Detection.

Optionally, check Save VCA Picture to save the captured unattended baggage detection pictures.

Follow these steps to set the detection rules and detection areas.

- Select an Arming Region to configure. Up to 4 regions are selectable.

- Drag the sliders to set Time Threshold and Sensitivity.

Time Threshold: The time of the objects are left in the region. If the value is 10, an alarm is triggered after the object is left and stayed in the region for 10s. Its range is [5s-20s].

Sensitivity: Similarity of the background image to the object. The higher the value, the more easily the detection alarm will be triggered.

- Click Draw Region and draw a quadrilateral in the preview window by specifying four vertices of the detection region.

Set the arming schedule. Refer to Chapter 11.1 Configure Arming Schedule.

Set the linkage actions. Refer to Chapter 11.2 Configure Alarm Linkage Actions.

Click Apply.

## Object Removal Detection

Purpose

The Object Removal Detection function detects the objects removed from a pre-defined region, such as the exhibits on display, and a series of actions can be taken when the alarm is triggered.

Go to System > Event > Smart Event.

Click Object Removable.

Object Removal Detection

Select a camera to configure.

Check Enable Object Removable Detection.

Optionally, check Save VCA Picture to save the captured object removable detection pictures.

Follow these steps to set the detection rules and detection areas.

- Select an Arming Region to configure. Up to 4 regions are selectable.

Drag the sliders to set Time Threshold and Sensitivity.

Time Threshold: The time of the objects removed from the region. If the value is 10, alarm will be triggered after the object disappears from the region for 10s. Its range is [5s-20s].

Sensitivity: The similarity degree of the background image. If the sensitivity is high, a very small object taken from the region will trigger the alarm.

Click Draw Region and draw a quadrilateral in the preview window by specifying four vertices of the detection region.

Set the arming schedule. Refer to Chapter 11.1 Configure Arming Schedule.

Set the linkage actions. Refer to Chapter 11.2 Configure Alarm Linkage Actions.

Click Apply.

## Audio Exception Detection

Purpose

Audio exception detection detects abnormal sounds in the surveillance scene, such as a sudden increase/decrease in sound intensity.

Go to System > Event > Smart Event.

Click Audio Exception.

Audio Exception Detection

Select a camera to configure.

Optionally, check Save VCA Picture to save the captured audio exception detection pictures.

Set the detection rules:

- Select the Exception Detection tab.

- Check Audio Loss Exception, Sudden Increase of Sound Intensity Detection, and/or Sudden Decrease of Sound Intensity Detection.

Audio Loss Exception: Detects a steep sound rise in the surveillance scene. You can set the detection sensitivity and threshold for steep sound rise by configuring its Sensitivity and Sound Intensity Threshold.

Sensitivity: The smaller the value, the more severe the change must be to trigger the detection. Range [1-100].

Sound Intensity Threshold: It can filter the sound in the environment. The louder the environment sound, the higher the value should be. Adjust it according to the environment. Range [1-100].

Sudden Decrease of Sound Intensity Detection: Detects a steep sound drop in the surveillance scene. You need set the detection sensitivity [1-100].

Set the arming schedule. Refer to Chapter 11.1 Configure Arming Schedule.

Set the linkage actions. Refer to Chapter 11.2 Configure Alarm Linkage Actions.

Click Apply.

## Sudden Scene Change Detection

Purpose

Scene change detection detects the change of the surveillance environment affected by external factors, such as the intentional rotation of the camera.

Go to System > Event > Smart Event.

Click Sudden Scene Change.

Sudden Scene Change

Select a camera to configure.

Check Enable Sudden Scene Change Detection.

Optionally, check Save VCA Picture to save the captured sudden scene change detection pictures.

Drag the Sensitivity slider to set the detection sensitivity. Sensitivity range: [1-100]. The higher the value, the more easily the change of scene can trigger the alarm.

Set the arming schedule. Refer to Chapter 11.1 Configure Arming Schedule.

Set the linkage actions. Refer to Chapter 11.2 Configure Alarm Linkage Actions.

Click Apply.

## Defocus Detection

Purpose

Image blur caused by lens defocus can be detected.

Go to System > Event > Smart Event.

Click Defocus.

Defocus Detection

Select a camera to configure.

Check Enable Defocus Detection.

Optionally, check Save VCA Picture to save the captured defocus detection pictures.

Drag the Sensitivity slider to set the detection sensitivity. Sensitivity range: [1-100]. The higher the value, the more easily the defocus image will be detected.

Set the arming schedule. Refer to Chapter 11.1 Configure Arming Schedule.

Set the linkage actions. Refer to Chapter 11.2 Configure Alarm Linkage Actions.

Click Apply.

## PIR Alarm

Purpose

A PIR (Passive Infrared) alarm is triggered when an intruder moves within the detector vision field. The heat energy dissipated by a person or any other warm blooded creature such as dogs, cats, etc., can be detected.

Go to System > Event > Smart Event.

Click PIR Alarm.

FIR Alarm

Select a camera to configure.

Check PIR Alarm.

Optionally, check Save VCA Picture to save the captured of PIR alarm pictures.

Set the arming schedule. Refer to Chapter 11.1 Configure Arming Schedule.

Set the linkage actions. Refer to Chapter 11.2 Configure Alarm Linkage Actions.

.Click Apply.

## Thermal Camera Detection

The NVR supports the event detection modes of the thermal network cameras: fire and smoke detection, temperature detection, temperature difference detection, etc.

Before you start

Add the thermal network camera to your device and make sure the camera is activated.

Go to System > Event > Smart Event.

Select a thermal camera from the camera list.

(Optional) Check Save VCA Picture to save the captured pictures of detection.

Select an event detection (Temperature, etc.).

Set the arming schedule. Refer to Chapter 11.1 Configure Arming Schedule.

Set the linkage actions. Refer to Chapter 11.2 Configure Alarm Linkage Actions.

Click Apply.

# Smart Analysis

With the configured VCA detection, the device supports smart analysis for people counting and heat map.

## People Counting

Purpose

Counting calculates the number of people entering or leaving a certain configured area and creates daily/weekly/monthly/annual reports for analysis.

Go to Smart Analysis > Counting.

Select the camera.

Select the report type to Daily Report, Weekly Report, Monthly Report, or Annual Report.

Set the Date to analyze. The people counting graphic will show.

People Counting Interface

(Optional) Click Export to export the report in Microsoft Excel format.

## Heat Map

Purpose

Heat Map is a graphical representation of data. The heat map function is used to analyze how many people visited and stayed in a specific area.

The Heat Map function must be supported by the connected IP camera and the corresponding configuration must be set.

Go to Smart Analysis > Heat Map.

Select a camera.

Select the report type as Daily Report, Weekly Report, Monthly Report, or Annual Report.

Set the Data to analyze.

Heat Map Interface

Click Counting. The results will be displayed in graphics marked in different colors.

As shown in the figure above, red color block (255, 0, 0) indicates the most trafficked area, and blue color block (0, 0, 255) indicates the less-popular area.

(Optional) Click Export to export the statistics report in Microsoft Excel format.

# POS Configuration

The device can be connected to a POS machine/server, and receive a transaction message to overlay on the image during Live View or playback, as well as trigger a POS event alarm.

The POS feature is supported by DS-9600/7700/7600-I (/P) Series Device only.

## Configure POS Settings

### Configure POS Connection

Go to System > POS.

Click Add to enter the POS adding interface.

Select a POS device from the drop-down list.

Check Enable.

The number of POS devices supported by each device is the half of its number of channel, e.g., 8 POS devices are supported for the DS-9616NI-I8 model.

POS Settings

Select the POS protocol to Universal Protocol, EPSON, AVE, or NUCLEUS.

When a new protocol is selected, reboot the device to activate the new settings.

Universal Protocol

Click Advanced to expand more settings when selecting the universal protocol. You can set the start line identifier, line break tag, and end line tag for the POS overlay characters, and the case-sensitive property of the characters. You can also optionally check the filtering identifier and the XML protocol.

Universal Protocol Settings

EPSON

The fixed start and end line tag are used for EPSON protocol.

AVE

The fixed start and end line tag are used for AVE protocol. Serial port and virtual serial port connection types are supported.

- Click Custom to configure the AVE settings.

- Set the rule to VSI-ADD or VNET.

- Set the address bit of the POS message to send.

- Click OK to save the settings.

AVE Settings

NUCLEUS

- Click the Custom to configure the NUCLEUS settings.

- Enter the employee No., shift No., and the terminal No. in the field. The matching message sent from the POS device will be used as the valid POS data.

The NUCLEUS protocol must be used in the RS-232 connection communication.

Set the connection mode to TCP Reception, UDP Reception, Multicast, RS-232, USB-to-RS-232, or Sniff, and click Parameters to configure the parameters for each connection mode.

TCP Connection

- When using TCP connection, the port must be set from 1 to 65535, and the port for each POS machine must be unique.

- Set the Allowed Remote IP Address of the device sending the POS message.

TCP Connection Settings

UDP Connection

- When using UDP connection, the port must be set from 1 to 65535, and the port for each POS machine must be unique.

- Set the Allowed Remote IP Address of the device sending the POS message.

USB-to-RS-232 Connection

Configure the USB-to-RS-232 convertor port parameters, including the port serial number, baud rate, data bit, stop bit, parity, and flow ctrl.

USB-to-RS-232 Settings

RS-232 Connection

Connect the device and the POS machine via RS-232. The RS-232 settings can be configured in Menu>Configuration>RS-232. The Usage must be set to Transparent Channel.

Multicast Connection

When connecting the device and the POS machine via Multicast protocol, set the multicast address and port.

Sniff Connection

Connect the device and the POS machine via Sniff. Configure the source address and destination address settings.

Sniff Settings

### Configure POS Text Overlay

Go to System > POS.

Click Channel Linkage and Display tab.

Select the linked channel to overlay the POS characters.

Set the characters overlay for the enabled POS.

- Character encoding format: currently the Latin-1 format is available

- Overlay mode of the characters to display in scrolling or page mod

- Font size and font color

- Display time (sec) of the characters. The value ranges 5 -3600 sec.

- Timeout of POS event. The value ranges 5 -3600 sec. When the device has not received the POS message within the defined time, the transaction ends.

In the Privacy Settings, set the POS privacy information to not display on the image, e.g., the card number, user name, etc.

Result: The defined privacy information will be displayed using ***on the image instead.

(optional) Check the checkbox to enable the Overlay POS in Live View. When this feature is enabled, the POS information is overlaid on the Live View image.

Overlay Character Settings

Drag the frame to adjust the textbox size and position on POS settings interface preview screen.

Click Apply to activate the settings.

## Configure POS Alarm

Purpose

A POS event can trigger channels to start recording, or trigger full screen monitoring or an audio warning, notifying the surveillance center, send e-mail, etc.

Go to Storage > Recording Schedule.

Set the POS event’s arming schedule.

Go to System > POS.

Click Event Linkage on the POS adding or editing interface.

Select the normal linkage actions: full screen monitoring, audio warning, or send e-mail.

Select one or more alarm output(s) to trigger.

Select one or more channels to record or become full-screen monitoring when a POS alarm is triggered.

Set Trigger Cameras of POS

Click Apply to save the settings.

# Network Settings

## Configure TCP/IP Settings

Purpose

TCP/IP settings must be properly configured before you can operate the device will operate over a network.

### Device with Dual Network Interface

Go to System > Network > TCP/IP.

TCP/IP Settings

Select Net-Fault Tolerance or Multi-Address Mode under Working Mode.

Net-Fault Tolerance: The two NIC cards use the same IP address, and you can select the main NIC to LAN1 or LAN2. In this way, in case of one NIC card failure, the device will automatically enable the other standby NIC card so as to ensure the normal running of the system.

Multi-Address Mode: The parameters of the two NIC cards can be configured independently. You can select LAN1 or LAN2 under Select NIC for parameter settings. Select one NIC card as the default route. When the system connects with the extranet, the data will be forwarded through the default route.

Configure other IP settings as needed.

- Check Enable DHCP to obtain IP settings automatically if a DHCP server is available on the network.

- Valid MTU value range is 500 to 9676.

Click Apply.

### Device with a Single Network Interface

Go to System > Network > TCP/IP.

TCP/IP Settings

Configure network parameters as needed.

- Check Enable DHCP to obtain IP settings automatically if a DHCP server is available on the network.

- Valid MTU value range is 500 to 9676.

Click Apply.

## Configure Guarding Vision

Guarding Vision provides the mobile phone application and the service platform page (www.guardingvision.com) to access and manage your connected encoder, which enables you to get a convenient remote access to the surveillance system.

The Guarding Vision can be enabled via operation on SADP software, GUI and Web browser. We introduce the operation steps on GUI in this section.

Go to Configuration > Network > Advanced Settings > Platform Access.

Guarding Vision Settings

Check the Enable checkbox to activate the function.

Then the Service Terms page pops up as below.

Service Terms

- Create the verification code in the Verification Code text field.

- Confirm the verification code.

- Read Terms of Service and Privacy Policy before enabling the service.

- Click OK to save the settings and return to the Guarding Vision page.

Guarding Vision Settings

Guarding Vision is disabled by default.

The verification code is empty when the device leaves factory.

The verification code must contain 6 to 12 letters or numbers and is case sensitive.

Every time you enable Guarding Vision, the Service Terms page pops up and you should read Terms of Service and Privacy Policy before enabling it.

(Optional) If you want to customize the server, enable Custom and enter the Server Address in the text field.

Click Save.

After configuration, you can access and manage the DVR by your mobile phone or by the website (www.guardingvision.com).

For the iOS users, please scan the QR code below to download the Guarding Vision application for the subsequent operations.

QR Code for iOS Users

For the Android users, please scan the QR code below to download the Guarding Vision application for the subsequent operations. You must install googleplay on your Android mobile phone to skip to the address successfully.

QR Code for Android Users

Please refer to the help file on the official website (www.guardingvision.com) and the Guarding Vision Mobile Client User Manual for adding the device to Guarding Vision and more operation instructions.

## Configure DDNS

Purpose

You can set Dynamic DNS service for network access. Different DDNS modes are available: DynDNS, PeanutHull, and NO-IP.

Before You Start

You must register the DynDNS, PeanutHull, or NO-IP services with your ISP before configuring DDNS settings.

Go to System > Network > TCP/IP > DDNS.

Check Enable.

Select DynDNS under DDNS Type.

PeanutHull and NO-IP are also available under DDNS Type, and required information should be entered accordingly.

Enter Server Address for DynDNS (i.e., members.dyndns.org).

Under Device Domain Name, enter the domain name obtained from the DynDNS Website.

Enter the User Name and Password registered in the DynDNS Website.

DDNS Settings

Click Apply.

## Configure PPPoE

If the device is connected to the Internet through PPPoE, you need to configure the user name and password accordingly under System > Network > TCP/IP > PPPoE.

Contact your Internet service provider for details about PPPoE service.

## Configure NTP

Purpose

Connection to a network time protocol (NTP) server can be configured on your device to ensure the system’s date and time accuracy.

Go to System > Network > TCP/IP > NTP.

NTP Settings

Check Enable.

Configure NTP settings as need.

Interval (min): Time interval between two time synchronization with NTP server

NTP Server: IP address of the NTP server

NTP Port: Port of the NTP server

Click Apply.

## Configure SNMP

Purpose

You can configure SNMP settings to get device status and parameter information.

Before You Start

Download the SNMP software to receive device information via the SNMP port. By setting the trap address and port, the device is allowed to send alarm events and exception messages to the surveillance center.

Go to System > Network > Advanced > SNMP.

SNMP Settings

Check Enable. A message will pop up to notify about a possible security risk. Click Yes to continue.

Configure the SNMP settings as needed.

Trap Address: SNMP host IP address.

Trap Port: Port of the SNMP host.

Click Apply.

## Configure Email

Purpose

The system can be configured to send an e-mail notification to all designated users when a specified event occurs such as when an alarm or motion event is detected, the administrator password is changed, etc.

Before You Start

The device must be connected to a local area network (LAN) that contains an SMTP mail server. The network must also be connected to either an intranet or the Internet depending on the location of the e-mail accounts to which you want to send notifications.

Go to System > Network > Advanced > Email.

E-mail Settings

Configure the following e-mail settings.

Enable Server Authentication: Check to enable the function if the SMTP server requires user authentication, and enter the user name and password accordingly.

SMTP Server: IP address of SMTP Server or host name (e.g., smtp.263xmail.com).

SMTP Port: The default TCP/IP port used for SMTP is 25.

Enable SSL/TLS: Check to enable SSL/TLS if required by the SMTP server.

Sender: The sender’s name.

Sender's Address: The sender's Address.

Select Receivers: Select the receiver. Up to 3 receivers can be configured.

Receiver: The receiver’s name.

Receiver's Address: The e-mail address of the user to be notified.

Enable Attached Picture: Check to send e-mail with attached alarm images. The interval is the time between sending two subsequent alarm images.

Click Apply.

(Optional) Click Test to send a test e-mail.

## Configure Ports

You can configure different types of ports to enable relevant functions.

Go to System > Network > Advanced > More Settings and configure port settings as needed.

Alarm Host IP/Port: With a remote alarm host configured, the device will send the alarm event or exception message to the host when an alarm is triggered. The remote alarm host must have the client management system (CMS) software installed.

The Alarm Host IP refers to the IP address of the remote PC on which the CMS software (e.g., iVMS-4200) is installed, and the Alarm Host Port (7200 by default) must be the same as the alarm monitoring port configured in the software.

Server Port: Server port (8000 by default) should be configured for remote client software access and its valid range is 2000 to 65535.

HTTP Port: HTTP port (80 by default) should be configured for remote Web browser access.

Multicast IP: Multicast can be configured to enable Live View for cameras that exceed the maximum number allowed through network. A multicast IP address covers Class-D IP ranging from 224.0.0.0 to 239.255.255.255 and it is recommended to use an IP address ranging from 239.252.0.0 to 239.255.255.255.

When adding a device to the CMS software, the multicast address must be the same as that of the device.

RTSP Port: RTSP (Real Time Streaming Protocol) is a network control protocol designed to control streaming media servers. The port is 554 by default.

Port Settings

# Hot Spare Device Backup

Purpose

The device can form an N+1 hot spare system. The system consists of several working devices and a hot spare device; when the working device fails, the hot spare device switches into operation, thus increasing the reliability of the system. Contact your dealer for details of models that support the hot spare function.

A bidirectional connection shown in the figure below is required to be built between the hot spare device and each working device.

Building a Hot Spare System

Before You Start

At least 2 devices must be online.

## Set Hot Spare Device

Purpose

Hot spare devices takes over working device tasks when working devices fail.

Go to System > Hot Spare.

Set the Work Mode to Hot Spare Mode.

Hot Spare

Click Apply.

Click Yes in the popup attention box to reboot the device.

The camera connection will be disabled when the device works in hot spare mode.

It is highly recommended to restore the device defaults after switching the working mode of the hot spare device to normal mode to ensure the normal operation afterwards.

## Set Working Device

Go to System > Hot Spare.

Set the Work Mode to Normal Mode.

Check Enable.

Enter the IP address, user name, and admin password of the hot spare device.

Hot Spare

Click Apply.

## Manage Hot Spare System

Go to System > Hot Spare in the hot spare device.

Check working devices on the device list and click Add to link the working device to the hot spare device.

A hot spare device can connect up to 32 working devices.

Figure 16-4 Add Working Device

Working Status Descrption

| Working Status | Description |
| --- | --- |
| No record | The working device works properly. |
| Backing up | If the working device goes offline, the hot spare device will record the video of the IP camera connected to the working device for backup The record back up functions for 1 working device at a time. |
| Synchronizing | When the working device comes back online, the lost video files will be restored by the record synchronization function. The record synchronization function can be enabled for 1 working device at a time. |

# User Management and Security

## Manage User Accounts

Purpose

The Administrator user name is admin and the password is set when you start the device for the first time. The Administrator has the permission to add and delete users and configure user parameters.

### Add a User

Go to System > User.

User Management Interface

Click Add to enter the operation permission interface.

Input the admin password and click OK.

In the Add User interface, enter the information for a new user, including User Name, Password, Confirm (password), User Level (Operator/Guest), and User’s MAC Address.

Add User

Strong Password Recommended–We highly recommend you create a strong password of your own choosing (using a minimum of 8 characters, including at least three of the following categories: upper case letters, lower case letters, numbers, and special characters) in order to increase the security of your product. We also recommend that you reset your password regularly. Especially in the high security systems, resetting the password monthly or weekly can better protect your product.

User Level: Set the user level to Operator or Guest. Different user levels have different operating permission.

Operator: An Operator user level has Two-way Audio permission in Remote Configuration and all operating permissions in Camera Configuration by default.

Guest: The Guest user has no permission of Two-way Audio in Remote Configuration and only has the local/remote playback in the Camera Configuration by default.

User’s MAC Address: The MAC address of the remote PC that logs onto the device. If it is configured and enabled, it allows only the remote user with this MAC address to access the device.

Click OK to finish adding the new user account.

In the User Management interface, the added new user is displayed on the list.

User List

### Edit the Admin User

You can modify the admin user account’s password and unlock pattern.

Go to System > User.

Select the admin user from the list and click Modify.

Edit User (Admin)

Edit the admin user information as desired, including a new admin password (strong password is required) and MAC address.

Edit the unlock pattern for the admin user account.

- Check Enable Unlock Pattern to enable the use of an unlock pattern when logging in to the device.

Use the mouse to draw a pattern among the 9 dots on the screen, and release the mouse when the pattern is done.

Refer to Chapter 2.2 Step 2for detailed instructions.

Click  of Export GUID to enter the reset password interface to export the GUID file for the admin user account.

When the admin password is changed, export the new GUID to the connected USB flash disk in the Import/Export interface for the future password resetting.

Set the security questions.

Click OK to save the settings.

For an Operator or Guest user account, click  on the user management interface to edit the permissions.

### Edit an Operator/Guest User

You can edit the user information, including user name, password, permission level, and MAC address. Check Change Password to change the password, and input the new password in the text field of Password and Confirm. A strong password is recommended.

Go to System > User.

Select a user from the list and click Modify.

Edit User (Operator/Guest)

Edit the user information as desired, including the new password (strong password is required) and MAC address.

### Delete a User

The admin user account has the permission to delete an operator/guest user account.

Go to System > User.

Select a user from the list.

Click Delete to delete the selected user account.

## Manage User Permissions

### Set User Permissions

For an added user, you can assign the different permissions, including local and remote operation of the device.

Go to System > User.

Select a user from the list, and then click  to enter the permission settings interface.

User Permission Settings Interface

Set the user’s operating permissions for Local Configuration, Remote Configuration, and Camera Configuration for the user.

Local Configuration

- Local Log Search: Searching and viewing logs and system information of device.

- Local Parameters Settings: Configuring parameters, restoring factory default parameters, and importing/exporting configuration files.

- Local Camera Management: Adding, deleting, and editing of IP cameras.

- Local Advanced Operation: Operating HDD management (initializing HDD, setting HDD property), upgrading system firmware, clearing I/O alarm output.

- Local Shutdown Reboot: Shutting down or rebooting the device.

Remote Configuration

- Remote Log Search: Remotely viewing logs that are saved on the device.

- Remote Parameters Settings: Remotely configuring parameters, restoring factory default parameters, and importing/exporting configuration files.

- Remote Camera Management: Remote adding, deleting, and editing of the IP cameras.

- Remote Serial Port Control: Configuring settings for RS-232 and RS-485 port settings.

- Remote Video Output Control: Sending remote button control signals.

- Two-Way Audio: Operating the two-way radio between the remote client and the device.

- Remote Alarm Control: Remotely arming (notify alarm and exception message to the remote client) and controlling the alarm output.

- Remote Advanced Operation: Remotely operating HDD management (initializing HDD, setting HDD property), upgrading system firmware, clearing I/O alarm output.

- Remote Shutdown/Reboot: Remotely shutting down or rebooting the device.

Camera Configuration

- Remote Live View: Remotely viewing live video of the selected camera(s).

- Local Manual Operation: Locally starting/stopping manual recording and alarm output of the selected camera(s).

- Remote Manual Operation: Remotely starting/stopping manual recording and alarm output of the selected camera(s). Local Playback: Locally playing back recorded files of the selected camera(s).

- Remote Playback: Remotely playing back recorded files of the selected camera(s).

- Local PTZ Control: Locally controlling PTZ movement of the selected camera(s).

- Remote PTZ Control: Remotely controlling PTZ movement of the selected camera(s).

- Local Video Export: Locally exporting recorded files of the selected camera(s).

- Local Live View: View live video of the selected camera(s) in local.

Click OK to save the settings.

Only the admin user account has the permission to restore factory default parameters.

### Set Local Live View Permission for Non-Admin Users

The admin user can assign to normal users (Operator or Guest) the live view permission for specific cameras.

Go to System > User.

Click  of the admin user.

Input admin password and click OK.

Select cameras that a non-admin user can view locally and click OK.

Set Live View Permissions

Click  of non-admin user.

Click the Camera Configuration tab.

Select Camera Permission as Local Live View.

Select cameras to display in Live View.

Click OK.

### Set Live View Permission on Lock Screen

The admin user can set live view permission for specific cameras in the screen lock status of device.

Go to System > User.

Click Live View Permission on Lock Screen.

Input admin password and click Next.

Set Live View Permissions on Lock Screen

Set the permissions.

- Select the camera (s) to allow live view when the current user account is in logout status.

- Deselect the camera (s) to forbidden the camera (s) being viewed when the current user account is in logout status.

Click OK.

The admin user can set this permission for user accounts.

When the normal user (Operator or Guest) has no local live view permission for specific camera (s) (refer to 17.2.2 Set Local Live View Permission for Non-Admin Users), the live view permission for such camera (s) on lock screen status cannot be configured (live view not allowed by default).

## Configure Password Security

### Export GUID File

The GUID file may help you to reset password when you forget password.

Select to export GUID file when you are activating the device, or editing the admin user account.

Insert the U flash disk to your device, and export the GUID file to the U flash disk.

Export GUID File

Please keep your GUID file properly for future password resetting.

### Configure Security Questions

The security question configuration may help you to reset password when you forget your password or encounter security issues.

Click Security Question Configuration when you are activating the device, or editing the admin user account.

Select three security questions from the drop-down list and input the answers.

Click OK.

Configure Security Questions

## Reset Password

When you forget the admin password, you can reset the password by importing the GUID file or by answering security questions.

### Reset Password by GUID

Before You Start

The GUID file must be exported and saved in the local U flash disk after you have activated the device or edited the admin user account. (Refer to Chapter 17.3.1 Export GUID File).

On the user login interface, click Forgot Password.

Select the password resetting type to Verify by GUID.

Please insert the U flash disk stored with the GUID file to the NVR before resetting password.

Select the GUID file from the U flash disk and click Import to import the file to the device.

If you have imported the wrong GUIE file for 7 times, you will be not allowed to reset the password for 30 minutes.

After the GUID file is successfully imported, enter the reset password interface to set the new admin password.

Click OK to set the new password. You can export the new GUID file to the U flash disk for future password resetting.

When the new password is set, the original GUID file will be invalid. The new GUID file should be exported for future password resetting. You can also enter the User>User Management interface to edit the admin user and export the GUID file.

### Reset Password by Security Questions

Before You Start

You have configured the security questions when you activate the device or edit the admin user account. (Refer to Chapter 17.3.2 Configure Security Questions).

On the user login interface, click Forgot Password.

Select the password resetting type to Verify by Security Question.

Input the correct answers of the three security questions.

Click OK.

If the answers mismatch, the verification is failed.

Create the new admin password on the Reset Password interface.

# System Service Maintenance

## Storage Device Maintenance

### Configure Disk Clone

Purpose

Select the HDDs to clone to the eSATA HDD.

Before You Start

Connect an eSATA disk to the device.

Go to Maintenance > HDD Operation > HDD Clone.

HDD Clone

Check the HDD to clone. The capacity of the selected HDD must match the capacity of the clone destination.

Click Clone.

Click Yes on the popup message box to create the clone.

Message Box

### S.M.A.R.T. Detection

Purpose

HDD detection functions such as the adopting of the S.M.A.R.T. and the Bad Sector Detection techniques. S.M.A.R.T. (Self-Monitoring, Analysis and Reporting Technology) are HDD monitoring systems to detect various reliability indicators in the hopes of anticipating failures.

Go to Maintenance > HDD Operation > S.M.A.R.T.

Select the HDD to view its S.M.A.R.T. information list.

Select the self-test types as Short Test, Expanded Test, or the Conveyance Test.

Click Self-Test to start the S.M.A.R.T. HDD self-evaluation.

The related S.M.R.T. information of the S.M.A.R.T. is shown, and you can check the HDD status.

S.M.A.R.T. Settings Interface

To use the HDD even when the S.M.A.R.T. checking has failed, check Continue to use the disk when self-evaluation is failed checkbox.

### Bad Sector Detection

Go to Maintenance > HDD Operation > Bad Sector Detection.

Select the HDD No. you want to configure in the dropdown list.

Select All Detection or Key Area Detection as the detection type.

Click the Self-Test button to start the detection.

Bad Sector Detection

- You can pause/resume or cancel the detection.

- After testing has been completed, you can click Error information to see the detailed damage information.

### HDD Health Detection

Purpose

You can view the health status of a 4 TB to 8 TB Seagate HDD that generated after October 1, 2017. Use this function to help troubleshoot HDD problems. Health Detection shows a more detailed HDD status than the S.M.A.R.T. function.

Go to Maintenance > HDD Operation > Health Detection.

Health Detection

Click an HDD to view details.

## Search and Export Log Files

Purpose

The device operation, alarm, exception, and information can be stored in log files, which can be viewed and exported at any time.

### Search the Log Files

Go to Maintenance > Log Information.

Figure 18-6 Log Search Interface

Set the log search conditions, including the time, major type and minor type.

Click Search to start searching the log files.

The matched log files will be displayed on the list, as shown below.

Figure 18-7 Log Search Results

Up to 2,000 log files can be displayed each time.

Step 5 Related Operation:

- Click  or double-click it to view detailed information.

- Click  to view the related video file.

### Export the Log Files

Before You Start

Connect a storage device to the NVR.

Search the log files. Refer to Chapter 18.2.1 Search the Log Files.

Select the log files you want to export, and click Export or click Export ALL on the Log Search interface to export all the system logs to the storage device.

Export Log Files

On the Export interface, select the storage device from Device Name.

Select the format of the log files to be exported. Up to 15 formats are selectable.

Click Export to export the log files to the selected storage device.

- Click the New Folder button to create a new folder in the storage device.

- Click the Format button to format the storage device before exporting the log(s).

## Import/Export IP Camera Configuration Files

Purpose

The IP camera information, including the IP address, manage port, password of admin, etc., can be saved in Microsoft Excel format and backed up to the local device. The exported file can be edited on a PC, including adding or deleting the content, and copying the setting to other devices by importing the Excel file to it.

Before You Start

When importing the configuration file, connect the storage device that contains the configuration file to the NVR.

Go to Camera > IP Camera Import/Export.

Click the IP Camera Import/Export tab, and the detected external device contents appear.

Export or import the IP camera configuration files.

- Click Export to export the configuration files to the selected local backup device.

- To import a configuration file, select the file from the selected backup device and click Import.

After the importing process is completed, you must reboot the device to activate the settings.

## Import/Export Device Configuration Files

Purpose

The device configuration files can be exported to a local device for backup; and the configuration files of one device can be imported to multiple devices if they are to be configured with the same parameters.

Before You Start

Connect a storage device to your device. To import the configuration file, the storage device must contain the file.

Go to Maintenance >Import/Export.

Import/Export Config File

Export or import the device configuration files.

- Click Export to export configuration files to the selected local backup device.

- To import a configuration file, select the file from the selected backup device and click the Import.

After having finished importing configuration files, the device will reboot automatically.

## Configure System Services

### Control4 Protocol

The Control4 protocol enables you to search the Hikvision devices via SDDP, get the basic network parameters, device information, or access some device operations.

Go to Menu > Maintenance > System Service > More Settings > Control4.

Check the checkbox of Enable SDDP or Enable CGI.

Click Apply.

### I-VIEW-NOW UPNP Reporting

The I-VIEW-NOW UPNP Reporting service allows the system to automatically send the device network parameters to authorized receivers by e-mail.

Go to Menu > Maintenance > System Service > More Settings > I-VIEW-NOW UPNP Reporting.

Check the checkbox of I-VIEW-NOW UPNP Reporting.

Click Apply.

## Configure Stream Encryption

The stream encryption enables to encrypt the streams for live view, playback, download, backup, etc.

Go to Menu > Maintenance > System Service > Stream Encryption.

Check Enable Stream Encryption.

Create the encryption password.

The stream encryption password is synchronized with the Hik-Connect service verification code. After enabling the encryption code, the Hik-Connect stream will be forcedly encrypted. Make sure the Hik-Connect service supports the stream encryption as well.

## Upgrade the System

Purpose

The firmware on your device can be upgraded with a local backup device or remote FTP server.

### Upgrade with a Local Backup Device

Before You Start

Connect your device to a local storage device that contains the firmware update file.

Go to Maintenance>Upgrade.

Click the Local Upgrade tab to enter the local upgrade interface.

Local Upgrade Interface

Select the firmware update file from the storage device.

Click Upgrade to start upgrading.

After the upgrade is complete, the device will reboot automatically to activate the new firmware.

### Upgrade by FTP

Before You Start

Ensure the network connection of the PC (running FTP server) and the device are valid and correct. Run the FTP server on the PC and copy the firmware into the corresponding directory of your PC.

Go to Maintenance>Upgrade.

Click the FTP tab to enter the local upgrade interface.

FTP Upgrade Interface

Enter FTP Server Address in the text field.

Click Upgrade to start upgrading.

After the upgrading is complete, reboot the device to activate the new firmware.

## Restore Default Settings

Go to Maintenance > Default.

Restore Defaults

Select the restore type from the following three options.

Restore Defaults: Restore all parameters, except the network (including IP address, subnet mask, gateway, MTU, NIC working mode, default route, server port, etc.) and user account parameters, to the factory default settings.

Factory Defaults: Restore all parameters to the factory default settings.

Restore to Inactive: Restore the device to inactive status.

The device will reboot automatically after restoring to the default settings.

# General System Settings

## Configure General Settings

Purpose:

You can configure the BNC output standard, VGA output resolution, and mouse pointer speed in the System > General interface.

Go to System > General.

General Settings Interface

Configure the following settings.

Language: The default language used is English.

Output Standard: Set the output standard to NTSC or PAL, which must be the same as the video input standard.

Resolution: Configure video output resolution.

Device Name: Edit device name.

Device No.: Edit the device serial number. The Device No. can be set in the range of 1 to 255, and the default No. is 255. The number is used for the remote and keyboard control.

Auto Logout: Set the timeout time for menu inactivity. E.g., when the timeout time is set to 5 minutes, then the system will exit from the current operation menu to Live View screen after 5 minutes of menu inactivity.

Mouse Pointer Speed: Set the speed of the mouse pointer; 4 levels are configurable.

Enable Wizard: Enable/disable the Wizard when the device starts up.

Enable Password: Enable/disable the use of the login password.

Click Apply to save the settings.

## Configure Date & Time

Go to System > General.

Configure the date and time.

Time Zone: Select the time zone.

Date Format: Select the date format.

System Date: Select the system date.

System Time: Set the system time.

Date and Time Settings

Click Apply to save the settings.

## Configure DST Settings

DST (daylight saving time) refers to the period of the year when clocks are moved one period ahead. In some areas worldwide, this has the effect of creating more sunlit hours in the evening during months when the weather is the warmest.

We advance our clocks ahead a certain period (depends on the DST bias you set) at the beginning of DST, and move them back the same period when we return to standard time (ST).

Go to System > General.

Check Enable DST.

DST Settings Interface

Set the DST mode to Auto or Manual.

- Auto: Automatically enable the default DST period according to the local DST rules.

- Manual: Manually set the start time and end time of the DST period, and the DST bias.

DST Bias: Set the time (30/60/90/120 minutes) offset from the standard time.

Example: DST begins at 2:00 a.m. on the second Sunday of March and ends at 2:00 a.m. on the first Sunday of November, with 60 minutes ahead.

Click Apply to save the settings.

# Appendix

## Glossary

- Dual Stream: Dual stream is a technology used to record high resolution video locally while transmitting a lower resolution stream over the network. The two streams are generated by the device, with the main stream having a maximum resolution of 4CIF and the sub-stream having a maximum resolution of CIF.

- HDD: Acronym for Hard Disk Drive. A storage medium which stores digitally encoded data on platters with magnetic surfaces.

- DHCP: Dynamic Host Configuration Protocol (DHCP) is a network application protocol used by devices (DHCP clients) to obtain configuration information for operation in an Internet Protocol network.

- HTTP: Acronym for Hypertext Transfer Protocol. A protocol to transfer hypertext request and information between servers and browsers over a network

- DDNS: Dynamic DNS is a method, protocol, or network service that provides the capability for a networked device, such as a router or computer system using the Internet Protocol Suite, to notify a domain name server to change, in real time (ad-hoc) the active DNS configuration of its configured hostnames, addresses or other information stored in DNS.

- PPPoE: Stands for "Point-to-Point Protocol over Ethernet." PPPoE is a network configuration used for establishing a PPP connection over an Ethernet protocol.

- Hybrid device: A hybrid device is a combination of a DVR and device.

- NTP: Acronym for Network Time Protocol. A protocol designed to synchronize the clocks of computers over a network.

- NTSC: Acronym for National Television System Committee. NTSC is an analog television standard used in such countries as the United States and Japan. Each frame of an NTSC signal contains 525 scan lines at 60Hz.

- Device: Acronym for Network Video Recorder. A device can be a PC-based or embedded system used for centralized management and storage for IP cameras, IP Domes and other devices.

- PAL: Acronym for Phase Alternating Line. PAL is also another video standard used in broadcast televisions systems in large parts of the world. PAL signal contains 625 scan lines at 50Hz.

- PTZ: Acronym for Pan, Tilt, Zoom. PTZ cameras are motor driven systems that allow the camera to pan left and right, tilt up and down and zoom in and out.

- USB: Acronym for Universal Serial Bus. USB is a plug-and-play serial bus standard to interface devices to a host computer.

## Troubleshooting

No image displayed on the monitor after starting up normally.

Possible Reasons:

No VGA or HDMI connections.

Connection cable is damaged.

Input mode of the monitor is incorrect.

Verify the device is connected with the monitor via HDMI or VGA cable.

If not, please connect the device with the monitor and reboot.

Verify the connection cable is good.

If there is still no image display on the monitor after rebooting, please check if the connection cable is good, and change a cable to connect again.

Verify Input mode of the monitor is correct.

Please check the input mode of the monitor matches with the output mode of the device (e.g. if the output mode of device is HDMI output, then the input mode of monitor must be the HDMI input). And if not, please modify the input mode of monitor.

Check if the fault is solved by the step 1 to step 3.

If it is solved, finish the process.

If not, please contact the engineer from our company to do the further process.

There is an audible warning sound “Di-Di-Di-DiDi” after a new bought device starts up.

Possible Reasons:

No HDD is installed in the device.

The installed HDD has not been initialized.

The installed HDD is not compatible with the device or is broken-down.

          - Verify at least one HDD is installed in the device.

If not, please install the compatible HDD.

Please refer to the Quick Start Guide for the HDD installation steps.

If you don’t want to install a HDD, go to Menu>System> Event>Normal Event>Exception, and uncheck the Audible Warning checkbox of “HDD Error”.

Verify the HDD is initialized.

- Go to Menu>Storage>Storage Device.

If the status of the HDD is “Uninitialized”, please check the checkbox of corresponding HDD and click the “Init” button.

Verify the HDD is detected or is in good condition.

- Select Menu>Storage>Storage Device.

- If the HDD is not detected or the status is “Abnormal”, please replace the dedicated HDD according to the requirement.

Check if the fault is solved by the step 1 to step 3.

If it is solved, finish the process.

If not, please contact the engineer from our company to do the further process.

The status of the added IP camera displays as “Disconnected” when it is connected through Private Protocol. Select “Menu>Camera>Camera>IP Camera” to get the camera status.

Possible Reasons:

Network failure, and the device and IP camera lost connections.

The configured parameters are incorrect when adding the IP camera.

Insufficient bandwidth.

          - Verify the network is connected.

- Connect the device and PC with the RS-232 cable.

Open the Super Terminal software, and execute the ping command. Input “ping IP” (e.g. ping 172.6.22.131).

Simultaneously press Ctrl and C to exit the ping command.

If there exists return information and the time value is little, the network is normal.

Verify the configuration parameters are correct.

- Go to Menu>Camera.

Verify the following parameters are the same with those of the connected IP devices, including IP address, protocol, management port, user name and password.

Verify the whether the bandwidth is enough.

- Go to Menu>Maintenance>Net Detect>Network Stat..

Check the usage of the access bandwidth, and see if the total bandwidth has reached its limit.

Check if the fault is solved by the step 1 to step 3.

If it is solved, finish the process.

If not, please contact the engineer from our company to do the further process.

- The IP camera frequently goes online and offline and the status of it displays as “Disconnected”.

Possible Reasons:

The IP camera and the device versions are not compatible.

Unstable power supply of IP camera.

Unstable network between IP camera and device.

Limited flow by the switch connected with IP camera and device.

          - Verify the IP camera and the device versions are compatible.

- Go to Menu>Camera, and view the firmware version of connected IP camera.

- Go to Menu>Maintenance>System Info>Device Info and view the firmware version of device.

Verify power supply of IP camera is stable.

- Verify the power indicator is normal.

When the IP camera is offline, please try the ping command on PC to check if the PC connects with the IP camera.

Verify the network between IP camera and device is stable.

When the IP camera is offline, connect PC and device with the RS-232 cable.

Open the Super Terminal, use the ping command and keep sending large data packages to the connected IP camera, and check if there exists packet loss.

Simultaneously press Ctrl and C to exit the ping command.

Example: Input ping 172.6.22.131 –l 1472 –f.

          - Verify the switch is not flow control.

Check the brand, model of the switch connecting IP camera and device, and contact with the manufacturer of the switch to check if it has the function of flow control. If so, please turn it down.

Check if the fault is solved by the step 1 to step 4.

If it is solved, finish the process.

If not, please contact the engineer from our company to do the further process.

No monitor connected with the device locally and when you manage the IP camera to connect with the device by web browser remotely, of which the status displays as Connected. And then you connect the device with the monitor via VGA or HDMI interface and reboot the device, there is black screen with the mouse cursor.

Connect the device with the monitor before startup via VGA or HDMI interface, and manage the IP camera to connect with the device locally or remotely, the status of IP camera displays as Connect. And then connect the device with the CVBS, and there is black screen either.

Possible Reasons:

After connecting the IP camera to the device, the image is output via the main spot interface by default.

          - Enable the output channel.

Go to Menu>System>Live View>General, and select video output interface in the drop-down list and configure the window you want to view.

The view settings can only be configured by the local operation of device.

Different camera orders and window-division modes can be set for different output interfaces separately, and digits like “D1”and “D2” stands for the channel number, and “X” means the selected window has no image output.

Check if the fault is solved by the above steps.

If it is solved, finish the process.

If not, please contact the engineer from our company to do the further process.

Live view stuck when video output locally.

Possible Reasons:

Poor network between device and IP camera, and there exists packet loss during the transmission.

The frame rate has not reached the real-time frame rate.

          - Verify the network between device and IP camera is connected.

When image is stuck, connect the RS-232 ports on PC and the rear panel of device with the RS-232 cable.

Open the Super Terminal, and execute the command of “ping 192.168.0.0 –l 1472 –f” (the IP address may change according to the real condition), and check if there exists packet loss.

Simultaneously press Ctrl and C to exit the ping command.

Verify the frame rate is real-time frame rate.

Go to Menu>Camera>Encoding Parameters, and set the Frame rate to Full Frame.

Check if the fault is solved by the above steps.

If it is solved, finish the process.

If not, please contact the engineer from our company to do the further process.

Live view stuck when video output remotely via the Internet Explorer or platform software.

Possible Reasons:

Poor network between device and IP camera, and there exists packet loss during the transmission.

Poor network between device and PC, and there exists packet loss during the transmission.

The performances of hardware are not good enough, including CPU, memory, etc..

Verify the network between device and IP camera is connected.

- When image is stuck, connect the RS-232 ports on PC and the rear panel of device with the RS-232 cable.

Open the Super Terminal, and execute the command of “ping 192.168.0.0 –l 1472 –f” (the IP address may change according to the real condition), and check if there exists packet loss.

Simultaneously press Ctrl and C to exit the ping command.

Verify the network between device and PC is connected.

- Open the cmd window in the Start menu, or you can press “windows+R” shortcut key to open it.

- Use the ping command to send large packet to the device, execute the command of “ping 192.168.0.0 –l 1472 –f” (the IP address may change according to the real condition), and check if there exists packet loss.

Simultaneously press Ctrl and C to exit the ping command.

Verify the hardware of the PC is good enough.

Simultaneously press Ctrl, Alt and Delete to enter the windows task management interface, as shown in the following figure.

Windows task management interface

Select the “Performance” tab; check the status of the CPU and Memory.

If the resource is not enough, please end some unnecessary processes.

Check if the fault is solved by the above steps.

If it is solved, finish the process.

If not, please contact the engineer from our company to do the further process.

When using the device to get the live view audio, there is no sound or there is too much noise, or the volume is too low.

Possible Reasons:

Cable between the pickup and IP camera is not connected well; impedance mismatches or incompatible.

The stream type is not set as “Video & Audio”.

The encoding standard is not supported with device.

          - Verify the cable between the pickup and IP camera is connected well; impedance matches and compatible.

Log in the IP camera directly, and turn the audio on, check if the sound is normal. If not, please contact the manufacturer of the IP camera.

Verify the setting parameters are correct.

Go to Menu>Camera>Encoding Parameters, and set the Stream Type as “Audio & Video”.

Verify the audio encoding standard of the IP camera is supported by the device.

The device supports G722.1 and G711 standards, and if the encoding parameter of the input audio is not one of the previous two standards, you can log in the IP camera to configure it to the supported standard.

Check if the fault is solved by the above steps.

If it is solved, finish the process.

If not, please contact the engineer from our company to do the further process.

The image gets stuck when device is playing back by single or multi-channel.

Possible Reasons:

Poor network between device and IP camera, and there exists packet loss during the transmission.

The frame rate is not the real-time frame rate.

The device supports up to 16-channel synchronize playback at the resolution of 4CIF, if you want a 16-channel synchronize playback at the resolution of 720p, the frame extracting may occur, which leads to a slight stuck.

Verify the network between device and IP camera is connected.

- When image is stuck, connect the RS-232 ports on PC and the rear panel of device with the RS-232 cable.

- Open the Super Terminal, and execute the command of “ping 192.168.0.0 –l 1472 –f” (the IP address may change according to the real condition), and check if there exists packet loss.

Simultaneously press the Ctrl and C to exit the ping command.

Verify the frame rate is real-time frame rate.

Select “Menu > Record > Parameters > Record”, and set the Frame Rate to “Full Frame”.

Verify the hardware can afford the playback.

Reduce the channel number of playback.

Go to Menu>Camera>Encoding Parameters, and set the resolution and bitrate to a lower level.

Reduce the number of local playback channel.

Go to Menu>Playback, and uncheck the checkbox of unnecessary channels.

Check if the fault is solved by the above steps.

If it is solved, finish the process.

If not, please contact the engineer from our company to do the further process.

No record file found in the device local HDD, and prompt “No record file found”.

Possible Reasons:

The time setting of system is incorrect.

The search condition is incorrect.

The HDD is error or not detected.

          - Verify the system time setting is correct.

Go to Menu>System>General, and verify the “Device Time” is correct.

Verify the search condition is correct.

Go to playback interface, and verify the channel and time are correct.

Verify the HDD status is normal.

Go to Menu>Storage>Storage Device to view the HDD status, and verify the HDD is detected and can be read and written normally.

Check if the fault is solved by the above steps.

If it is solved, finish the process.

If not, please contact the engineer from our company to do the further process.

## Summary of Changes

### Version 4.1.50

Added:

- Playback by video synopsis.

- Security questions configuration.

- Support event detection modes of thermal network cameras.

- Custom window-division live view layout configuration.

- System services: I-VIEW-NOW UPNP Reporting, Control4

- Stream encryption

### Version 4.1.10

- Optimize the GUI information design.

### Version 4.1.0

- Complete new GUI information design for more fluent and visual user experience.

- Files management and playback.

- HDD health monitoring for Seagate HDD.

### Version 3.4.92

Added:

- Easy network access by Guarding Vision.

Deleted:

- Delete two DDNS types: IP sever and HiDDNS.

### Version 3.4.91

Added:

- Support long distance (max.: 250-300 m) network transmission via PoE for /P models.

- Add prompt of using enterprise-level HDD to create array on GUI.

### Version 3.4.90

Added:

- Reset the admin password by exporting/importing the GUID file.

- DS-7600/7700/9600-I (/P) series device support 3D positioning in live view.

- Configurable main stream and sub-stream for the live view.

- All-day continuous recording is configured by factory default.

Updated:

- Optimize the playback interface and add the configurable motion detection area for smart playback.

- Up to 2048 LRP lists supported in vehicle detection.

### Version 3.4.80

Added:

- DS-7600/7700/9600-I (/P) series device is accessible by the thermal network camera, and supports the advanced search for fire/ship/temperature/temperature difference detection triggered alarm and the recorded video files and pictures.

- DS-7600/7700/9600-I (/P) series device supports the playback by main stream or sub stream.

- Remind user to remember the password after the device is activated.

- One-key alarm disarming for the local alarm input 1.

Updated:

- Optimize the playback by normal/smart interface.

- Admin Password changed to Password when adding the IP camera.

Deleted:

- Delete four VCA detection types: people gathering, fast movement, parking and loitering.

### Version 3.4.70

Added:

- Add the POS function.

### Version 3.4.6

Updated:

- Update the description of IR remote control operation.

### Version 3.4.2

Added:

- Support the display of IP camera’s password on the IP camera management interface.

- Add the configuration and use of unlock pattern for fast login.

- Add the fisheye expansion view for the connected fisheye camera in the live view and playback.

- Add the scaling display (30min/1h/2h/6h/24h) of time bar in the playback mode.

- Add the thumbnails view and fast view during playback.

Updated:

- Optimize the playback interface.

- Update the digital zoom operation in image.

### Version 3.3.9

Updated:

- Support H.265 video encoding format.

Deleted:

- Delete the PPPoE settings.

### Version 3.3.7

Added:

- Add the new models of DS-7700NI-K4(/P) and DS-7600NI-K2(/P).

- Add the front panel and rear panel of the new models.

- Add the specifications of the new models.

### Version 3.3.6

Added:

- Add front panel and rear panel of DS-9600NI-I16.

Updated:

- DS-9600NI-I16 supports RAID6, capture, picture playback, eSATA HDD and eSATA backup, two self-adaptive 10M/100M/1000M network interfaces.

### Version 3.3.4

Added:

- Add the new models of DS-7600NI-I2 (/P) and DS-7700NI-I4 (/P).

- Add the support of Cloud P2P.

## List of IP Cameras Connected to PoE by Long Network Cable (100 - 300 m)

| Index | Model |
| --- | --- |
| 1 | DS-2CD4665F-IZHS |
| 2 | DS-2CD4026FWD-AP |
| 3 | DS-2CD4A35FWD-IZHS |
| 4 | DS-2CD2642FWD-IZS |
| 5 | DS-2CD2F42FWD-IWS |
| 6 | DS-2CD2942F-IWS |
| 7 | DS-2CD2510F |
| 8 | DS-2CD2342WD-I |
| 9 | DS-2CD2322WD-I |
| 10 | DS-2CD2352-I |
| 11 | DS-2CD2642FWD-IZS |
| 12 | DS-2CD2642FWD-I |
| 13 | DS-2CD2642FWD-IS |
| 14 | DS-2CD2642FWD-IZ |
| 15 | DS-2CD2742FWD-IZS |
| 16 | DS-2CD2742FWD-I |
| 17 | DS-2CD2742FWD-IS |
| 18 | DS-2CD2742FWD-IZ |
| 19 | DS-2CD2T42WD-I8 |
| 20 | DS-2CD2T42WD-I5 |

040110171012

# Text boxes

Network Video Recorder

User Manual

Network Video Recorder

User Manual

UD09220N